## Slide 1: Embedded Computer Architecture 5SAI0 Instruction Level Parallel Architectures Part I
Henk Corporaal
www.ics.ele.tue.nl/~heco/courses/ECA
TUEindhoven
2021-2022

## Slide 2: Topics on ILP architectures
Introduction, Hazards (short recap)
Out-Of-Order (OoO) execution (H&P sect 3.4-3.6):
  Dependences limit ILP: dynamic scheduling
  Hardware speculation
Branch prediction (H&P sect 3.6 + 3.9)
Multiple issue (H&P sect 3.7-3.8)
How much ILP is there?
Material Ch 3 (H&P or Dubois, second part)

## Slide 3: What is ILP = Instruction level parallelism
multiple operations (or instructions) can be executed in parallel, from a single instruction stream
  so we are not yet talking about MIMD, multiple instruction streams
Needed:
Sufficient (HW) resources
Parallel scheduling
  Hardware solution
  Software solution
Application should contain sufficient ILP

## Slide 4: Single Issue RISC vs Superscalar
op
op
op
op
op
op
op
op
op
op
op
op
execute
1 instr/cycle
instr
instr
instr
instr
instr
instr
instr
instr
instr
instr
instr
instr
(1-issue)
RISC CPU
Change HW,
but can use
same code
op
op
op
op
op
op
op
op
op
op
op
op
issue and (try to) execute
3 instr/cycle
instr
instr
instr
instr
instr
instr
instr
instr
instr
instr
instr
instr
3-issue Superscalar

## Slide 5: Recap (from pipelining lectures): Hazards
Three types of hazards (see previous lecture)
  Structural
    Multiple instructions need access to the same hardware at the same time
  Data dependence
    There is a dependence between operands (in register or memory) of successive instructions
  Control dependence
    Determines the order of the execution of basic blocks
    When jumping/branching to another address the pipeline has to be (partly) squashed and refilled
Hazards cause scheduling problems and delay the pipeline

## Slide 6: Impact of Hazards
Hazards cause pipeline 'bubbles' Increase of CPI (and therefore execution time)
Texec = Ninstr * CPI * Tcycle
  where
  CPI = CPIbase + Σi <CPIhazard_i>
  <CPIhazard> = fhazard * <Cycle_penaltyhazard>
  fhazard = fraction [0..1] of occurrence of this hazard

## Slide 7: Data dependences (see earlier lectures for details & examples)
RaW read after write
  real or flow dependence
  can only be avoided by value prediction (i.e. speculating on the outcome of a previous operation)
WaR write after read
WaW write after write
  WaR and WaW are false or name dependencies
  Could be avoided by renaming (if sufficient registers are available); see later slide
Notes:
data dependences can be both between registers and memory data operations
data dependencies are shown in de DDG: Data Dependence Graph

## Slide 8: Control Dependences: CFG
C input code:
CFG (Control Flow Graph):
1
sub t1, a, b
bgz t1, 2, 3
4
mul y,a,b
…………..
3
rem r, b, a
goto 4
2
rem r, a, b
goto 4
if (a > b) { r = a % b; }
else { r = b % a; }
y = a*b;
Questions:
How real are control dependences?
Can ‘mul y,a,b’ be moved to block 2, 3 or even block 1?
Can ‘rem r, a, b’ be moved to block 1 and executed speculatively?

## Slide 9: Avoiding pipeline stalls due to Hazards
Structural
  Buy more hardware
    Extra units, pipelined units, more ports on RF and data memory (or banked memories), etc.
  Note: more HW means bigger chip => could increase cycle time tcycle
Data dependence
  Real (RaW) dependences: add Forwarding (aka Bypassing) logic
    Compiler optimizations
  False (WaR & WaW) dependences: use renaming (either in HW or in SW)
Control dependence
  Adding extra pipeline HW to reduce the number of Branch delay slots
  Branch prediction
  Avoiding Branches

## Slide 10: Topics on ILP architectures
Introduction, Hazards (short recap)
Out-Of-Order (OoO) execution:
  Dependences limit ILP: dynamic scheduling
  Hardware speculation
Branch prediction
Multiple issue
How much ILP is there?
Material Ch 3 (H&P or Dubois, second part)

## Slide 11: Let's look at Out-of-Order execution:
Dynamic Scheduling

## Slide 12: Dynamic Scheduling Principle
What we examined so far is static scheduling
  Compiler reorders instructions so as to avoid hazards and reduce stalls
Dynamic scheduling: hardware rearranges instruction execution to reduce stalls
Example:
    DIV.D F0,F2,F4 ; takes 24 cycles and
    ; is not pipelined
    ADD.D F10,F0,F8
    SUB.D F12,F8,F14
Key idea: Allow instructions behind stall to proceed
Book describes Tomasulo algorithm in detail, but we first describe general idea
This instruction cannot continue
even though it does not depend
on previous Div and Add
RaW; real dependence

## Slide 13: Advantages of Dynamic Scheduling (compared to static scheduling, by compiler)
Handles cases when dependences are unknown at compile time
  e.g., because they may involve a memory reference
Simplifies the compiler (although a good compiler helps)
Binary compatible: Allows code compiled for one machine to run efficiently on a different machine, with different number of function units (FUs), and different pipelining
Allows hardware speculation, a technique with significant performance advantages, that builds on dynamic scheduling
  Speculation = Doing something early, before you know it is really needed
  In processing: Executing instructions before control dependend branch is handled
    i.e., we speculate on the branch outcome

## Slide 14: Superscalar: General Architecture Concept
Instruction
Memory
Instruction
Cache
Decoder
Branch
Unit
ALU-1
ALU-2
Logic &
Shift
Load
Unit
Store
Unit
Reorder
Buffer
Register
File
Data
Cache
Data
Memory
Reservation Stations
Address
Data
Data
Instruction
N
N = issue rate

## Slide 15: Example of Superscalar Execution
Superscalar processor organization, example:
  simple pipeline: IF, EX, WB
  fetches/issues upto 2 instructions each cycle (= 2-issue)
  2 ld/st units, dual-ported memory; 2 FP adders; 1 FP multiplier
  Instruction window (buffer between IF and EX stage) is of size 2
  FP ld/st takes 1 cc; FP +/- takes 2 cc; FP * takes 4 cc; FP / takes 8 cc
Cycle 1 2 3 4 5 6 7
L.D F6,32(R2)
L.D F2,48(R3)
MUL.D F0,F2,F4
SUB.D F8,F2,F6
DIV.D F10,F0,F6
ADD.D F6,F8,F2
MUL.D F12,F2,F4

## Slide 16: Example of Superscalar Processor Execution
Superscalar processor organization:
  simple pipeline: IF, EX, WB
  fetches 2 instructions each cycle
  2 ld/st units, dual-ported memory; 2 FP adders; 1 FP multiplier
  Instruction window (buffer between IF and EX stage) is of size 2
  FP ld/st takes 1 cc; FP +/- takes 2 cc; FP * takes 4 cc; FP / takes 8 cc
Cycle 1 2 3 4 5 6 7
L.D F6,32(R2) IF
L.D F2,48(R3) IF
MUL.D F0,F2,F4
SUB.D F8,F2,F6
DIV.D F10,F0,F6
ADD.D F6,F8,F2
MUL.D F12,F2,F4

## Slide 17: Example of Superscalar Processor Execution
Superscalar processor organization:
  simple pipeline: IF, EX, WB
  fetches 2 instructions each cycle
  2 ld/st units, dual-ported memory; 2 FP adders; 1 FP multiplier
  Instruction window (buffer between IF and EX stage) is of size 2
  FP ld/st takes 1 cc; FP +/- takes 2 cc; FP * takes 4 cc; FP / takes 8 cc
Cycle 1 2 3 4 5 6 7
L.D F6,32(R2) IF EX
L.D F2,48(R3) IF EX
MUL.D F0,F2,F4 IF
SUB.D F8,F2,F6 IF
DIV.D F10,F0,F6
ADD.D F6,F8,F2
MUL.D F12,F2,F4

## Slide 18: Example of Superscalar Processor Execution
Superscalar processor organization:
  simple pipeline: IF, EX, WB
  fetches 2 instructions each cycle
  2 ld/st units, dual-ported memory; 2 FP adders; 1 FP multiplier
  Instruction window (buffer between IF and EX stage) is of size 2
  FP ld/st takes 1 cc; FP +/- takes 2 cc; FP * takes 4 cc; FP / takes 8 cc
Cycle 1 2 3 4 5 6 7
L.D F6,32(R2) IF EX WB
L.D F2,48(R3) IF EX WB
MUL.D F0,F2,F4 IF EX
SUB.D F8,F2,F6 IF EX
DIV.D F10,F0,F6 IF
ADD.D F6,F8,F2 IF
MUL.D F12,F2,F4

## Slide 19: Example of Superscalar Processor Execution
Superscalar processor organization:
  simple pipeline: IF, EX, WB
  fetches 2 instructions each cycle
  2 ld/st units, dual-ported memory; 2 FP adders; 1 FP multiplier
  Instruction window (buffer between IF and EX stage) is of size 2
  FP ld/st takes 1 cc; FP +/- takes 2 cc; FP * takes 4 cc; FP / takes 8 cc
Cycle 1 2 3 4 5 6 7
L.D F6,32(R2) IF EX WB
L.D F2,48(R3) IF EX WB
MUL.D F0,F2,F4 IF EX EX
SUB.D F8,F2,F6 IF EX EX
DIV.D F10,F0,F6 IF
ADD.D F6,F8,F2 IF
MUL.D F12,F2,F4
stall because
of data dep.
cannot be fetched because window full

## Slide 20: Example of Superscalar Processor Execution
Superscalar processor organization:
  simple pipeline: IF, EX, WB
  fetches 2 instructions each cycle
  2 ld/st units, dual-ported memory; 2 FP adders; 1 FP multiplier
  Instruction window (buffer between IF and EX stage) is of size 2
  FP ld/st takes 1 cc; FP +/- takes 2 cc; FP * takes 4 cc; FP / takes 8 cc
Cycle 1 2 3 4 5 6 7
L.D F6,32(R2) IF EX WB
L.D F2,48(R3) IF EX WB
MUL.D F0,F2,F4 IF EX EX EX
SUB.D F8,F2,F6 IF EX EX WB
DIV.D F10,F0,F6 IF
ADD.D F6,F8,F2 IF EX
MUL.D F12,F2,F4 IF

## Slide 21: Example of Superscalar Processor Execution
Superscalar processor organization:
  simple pipeline: IF, EX, WB
  fetches 2 instructions each cycle
  2 ld/st units, dual-ported memory; 2 FP adders; 1 FP multiplier
  Instruction window (buffer between IF and EX stage) is of size 2
  FP ld/st takes 1 cc; FP +/- takes 2 cc; FP * takes 4 cc; FP / takes 8 cc
Cycle 1 2 3 4 5 6 7
L.D F6,32(R2) IF EX WB
L.D F2,48(R3) IF EX WB
MUL.D F0,F2,F4 IF EX EX EX EX
SUB.D F8,F2,F6 IF EX EX WB
DIV.D F10,F0,F6 IF
ADD.D F6,F8,F2 IF EX EX
MUL.D F12,F2,F4 IF
cannot execute
structural hazard

## Slide 22: Example of Superscalar Processor Execution
Superscalar processor organization:
  simple pipeline: IF, EX, WB
  fetches 2 instructions each cycle
  2 ld/st units, dual-ported memory; 2 FP adders; 1 FP multiplier
  Instruction window (buffer between IF and EX stage) is of size 2
  FP ld/st takes 1 cc; FP +/- takes 2 cc; FP * takes 4 cc; FP / takes 8 cc
Cycle 1 2 3 4 5 6 7
L.D F6,32(R2) IF EX WB
L.D F2,48(R3) IF EX WB
MUL.D F0,F2,F4 IF EX EX EX EX WB
SUB.D F8,F2,F6 IF EX EX WB
DIV.D F10,F0,F6 IF EX
ADD.D F6,F8,F2 IF EX EX WB
MUL.D F12,F2,F4 IF ?

## Slide 23: Superscalar: General Architecture Concept
Instruction
Memory
Instruction
Cache
Decoder
Branch
Unit
ALU-1
ALU-2
Logic &
Shift
Load
Unit
Store
Unit
Reorder
Buffer
Register
File
Data
Cache
Data
Memory
Reservation Stations
Address
Data
Data
Instruction
N
N = issue rate

## Slide 24: Superscalar Issues
How to fetch multiple instructions in time? (especially across basic block boundaries)
Predicting branches
Non-blocking memory system
Tune #resources(#FUs, #ports on RF, Ld/St capacity, #entries, etc.)
Handling dependencies
How to support precise interrupts?
How to recover from a mis-predicted branch path?
For the latter two issues you may wish to look at speculative and architectural state ,
  Processor Microarchitecture by Antonio González e.a., Morgan&Claypool 2011
  Superscalar Microprocessor Design, Mike Johnson, 1991 (or thesis 1989)

## Slide 25: Beginning of dynamic scheduling
1967 @ IBM
  Robert Tomasulo
  Dynamic scheduling of Floating Point operations on multiple execution units
  Allowing Out-Of-Order execution
  Register renaming in HW
    Only a few architectural visible Floating Point registers were available
    Renaming extends this number (although not architectural visible)
  Reservation stations in front of Execution Units
  CDB: Common Data Bus for all result broadcasts
see https://en.wikipedia.org/wiki/Tomasulo_algorithm

## Slide 26: Tomasulo’s Algorithm
Top-level design:
Note: Load and Store buffers contain data and addresses, act like reservation stations

## Slide 27: Tomasulo’s Algorithm
3 basic steps:
Issue
  Get next instruction from FIFO queue
  If available RS (reservation station), issue instruction to the RS, with operand values if they are available
  If operand values not available, stall the instruction
Execute
  When operand becomes available, store it in all reservation stations waiting for it
  When all operands are ready, issue the instruction
  Loads and stores are maintained in program order
  No instruction allowed to initiate execution until all earlier branches (that precede it in program order) have completed
Write result
  Write result on CDB into reservation stations and store buffers
    (Stores must wait until address and value are received)

## Slide 28: Register Renaming: general idea
Example, look at F6:
DIV.D F0, F2, F4
ADD.D F6, F0, F8
S.D F6, 0(R1)
SUB.D F8, F10, F14
MUL.D F6, F10, F8
False (aka “name”) dependences with F6
  anti: WaR and
  output: WaW in this example
Question: how can this code (optimally) be executed?
F6: RaW
F6: WaR
F6: WaW

## Slide 29: Register Renaming Technique
Eliminate name/false dependencies:
  anti- (WaR) and output (WaW)) dependencies
Can be implemented
  by the compiler
    advantage: low cost
    disadvantage: “old” codes perform poorly
  by hardware
    advantage: binary compatibility
    disadvantage: extra hardware needed

## Slide 30: Register Renaming by HW
Same example after renaming:
  DIV.D R, F2, F4
  ADD.D S, R, F8
  S.D S, 0(R1)
  SUB.D T, F10, F14
  MUL.D U, F10, T
Each destination gets a new (physical) register assigned
Now only RaW hazards remain, which can be strictly ordered
We will see several HW implementations of Register Renaming
  use ReOrder Buffer (ROB) & Reservation Stations, or
  use large register file with mapping table
Original code:
DIV.D F0, F2, F4
ADD.D F6, F0, F8
S.D F6, 0(R1)
SUB.D F8, F10, F14
MUL.D F6, F10, F8

## Slide 31: Register Renaming with Tomasulo
Register renaming can be provided by reservation stations (RS)
  Each RS entry contains 3 fields:
    Instruction
    Buffered operand values (when available)
    Reservation station number of instruction providing the operand values
Operation of RS:
  RS fetches and buffers an operand as soon as it becomes available
    not necessarily involving register file
  Pending instructions designate the RS to which they will send their output
    Result values broadcast on a result bus, called the common data bus (CDB)
  Only the last output updates the register file
  As instructions are issued, the register-IDs are renamed with the reservation station
  We can have many more reservation stations than (architectural) registers

## Slide 32: Example
snapshot, first L.D just finished

## Slide 33: Speculation (Hardware based)
Execute instructions along predicted execution paths but only commit the results if the prediction was correct
Instruction commit: allowing an instruction to only update the register file when instruction is no longer speculative
Need an additional piece of hardware to prevent any irrevocable action until an instruction commits:
  Reorder buffer, or Large renaming register file
  why? think about it?

## Slide 34: Speculative OoO
NEW
execution with
speculation
using RoB

## Slide 35: Reorder Buffer (RoB)
RoB – holds the result of instruction between completion and commit
  Four fields per entry:
    Instruction type: branch/store/register
    Destination field: register number
    Value field: output value
    Ready field: completed execution?
      is the data valid
Modify reservation stations:
  Operand source-id is now RoB (if its producer is still in the RoB) instead of functional unit (check yourself!)

## Slide 36: Reorder buffer in operation
After finishing the two loads

## Slide 37: Reorder Buffer (RoB)
Register values and memory values are not written until an instruction commits
RoB effectively renames the destination registers
  every destination gets a new entry in the RoB
On misprediction:
  Speculated entries in RoB are cleared
Exceptions:
  Not recognized/taken until it is ready to commit
  Precise exceptions require that ‘later’ entries in RoB are cleared
Notes: precise exceptions require that instructions started earlier should complete, instructions started after the excepting instruction should be squased, before the exception is taken

## Slide 38: Register renaming
The RoB together with the Reservation station effectively implement register renaming => avoiding WaW and WaR Hazards when reordering code
But...
  there is an alternative.....

## Slide 39: Register Renaming using RAT
there’s a physical register file larger than logical (aka architectural)register file
mapping table associates logical registers with physical register
  called RAT = Register Alias Table
when an instruction is decoded:
  its physical source registers are obtained from mapping table
  its physical destination register is obtained from a free list
  mapping table is updated
addi r3,r3,4
R8
R7
R5
R1
R9
R2 R6
before:
current
mapping table:
current free list:
r0
r1
r2
r3
r4
addi R2,R1,4
R8
R7
R5
R2
R9
R6
after:
updated
mapping table:
new free list:
r0
r1
r2
r3
r4
ri
Ri
Logic RF
Physical RF

## Slide 40: Register Renaming using RAT: Another example:
Before (assume r0->R8, r1->R6, r2->R5, .. ):
    addi r1, r2, 1
    addi r2, r0, 0 // WaR
    addi r1, r2, 1 // WaW + RaW
After (free list: R7, R9, R10)
    addi R7, R5, 1
    addi R10, R8, 0 // WaR disappeared
    addi R9, R10, 1 // WaW disappeared, // RaW renamed to R10

## Slide 41: Summary O-o-O architectures
Instructions issue in-order, execute out-of-order, and commit in-order !!
Renaming avoids naming (false) dependences
  via RoB: allocating an entry for every result, or
  via Register Mapping: Architectural registers are mapped on (many more) Physical registers
Speculation beyond branches
  branch prediction required (see next slides)
  recovery needed in case of miss prediction
    in-order-completion
    also needed for precise exception support

## Slide 42: Topics on ILP architectures
Introduction, Hazards (short recap)
Out-Of-Order (OoO) execution:
Branch prediction
  1&2 bit prediction
  Branch correlation
  Avoiding branches: if-conversion
Multiple issue
How much ILP is there?
Material Ch 3 (H&P or Dubois, second part)

## Slide 43: Branch Prediction
what is it?
why do we need it?
how does it work?
various schemes
subi R3,R1,#2
b1: bnez R3,L1
add R1,R0,R0
subi R3,R2,#2
add R2,R0,R0
sub R3,R1,R2
Just a code example with branches:
can instructions after branch execute while branch outcome not yet known?

## Slide 44: Branch Prediction Principles
breq r1, r2, label // if r1==r2 // then PCnext = label
// else PCnext = PC + 4 (for a RISC)
Questions:
do I jump ? -> branch prediction
where do I jump ? -> branch target prediction
what's the average branch penalty?
  <CPIbranch_penalty>
  i.e. how many instruction slots do I miss (or squash) due to branches

## Slide 45: Branch Prediction & Speculation
High branch penalties in heavily pipelined processors:
  CPI = CPIbase + fbranch * fmisspredict * cycles_penalty
  Large impact if:
    long pipeline → cycles_penalty high
    multiple-issue processors → CPIbase low
Many branches; if no speculation, and about 20% of the instructions being a branch, the maximum ILP is five (but actually much less!)
Idea: predict the outcome of branches based on their history and execute instructions at the predicted branch target speculatively

## Slide 46: Branch Prediction Schemes
Predict branch direction:
1-bit Branch Prediction Buffer
2-bit Branch Prediction Buffer
Correlating Branch Prediction Buffer
Predicting next address:
Branch Target Buffer
Return Address Predictors
+ Or: try to get rid (some) of those malicious branches

## Slide 47: 1-bit Branch Prediction Buffer
1-bit branch prediction buffer or branch history table (BHT):
Buffer is like a cache without tags
Does not help for our MIPS pipeline because target address calculations performed in same stage as branch condition calculation
10…..10 101 00
0
1
0
1
0
1
1
0
PC
BHT
size=2k
k-bits

## Slide 48: Two 1-bit predictor problems
Aliasing: lower k bits of different branch instructions could be the same
  Solution: Use tags (just like in a cache); however very expensive; tag requires many more bits per entry
  Better: just accept this problem, and make table big
Loops are predicted wrong twice
  Solution: Use n-bit saturation counter prediction
    taken if counter  2 (n-1)
    not-taken if counter < 2 (n-1)
  A 2-bit saturating counter predicts a loop wrong only once
10…..10 101 00
0
1
0
1
0
1
1
0
PC
BHT
size=2k
k-bits

## Slide 49: 2-bit Branch Prediction Buffer
Solution: 2-bit scheme where prediction is changed only if mispredicted twice
Can be implemented as a saturating counter, e.g. as following state diagram:
T
T
NT
Predict Taken
Predict Not
Taken
Predict Taken
Predict Not
Taken
T
NT
T
NT
NT

## Slide 50: Next step: Correlating Branches
Fragment from SPEC92 benchmark eqntott:
if (aa==2)
aa = 0;
if (bb==2)
bb=0;
if (aa!=bb){..}
subi R3,R1,#2
b1: bnez R3,L1
add R1,R0,R0
L1: subi R3,R2,#2
b2: bnez R3,L2
add R2,R0,R0
L2: sub R3,R1,R2
b3: beqz R3,L3

## Slide 51: Correlating Branch Predictor
Idea: behavior of current branch is related to (taken/not taken) history of recently executed branches
  Then behavior of recent branches selects between, say, 4 predictions of next branch, updating just that prediction
(2,2) predictor: 2-bit global, 2-bit local
(k,n) predictor uses behavior of last k branches to choose from 2k predictors, each of which is n-bit predictor
  4 bits from branch address
2-bit global
branch history register
(01 = not taken, then taken)
2-bits per branch local predictors
Prediction
shift register,
remembers
last 2 branches

## Slide 52: Branch Correlation: the General Scheme
Table size (usually n = 2): Nbits = k * 2a + 2k * 2m *n
mostly n = 2
n-bit
saturating
Up/Down
Counter
Prediction
Branch Address
0
1
2k-1
0
1
2m-1
Branch History Table (BHT)
a
k
m
Pattern History Table
4 parameters: (a, k, m, n)

## Slide 53: Two varieties
GA: Global history, a = 0
  only one (global) history register  correlation is with previously executed branches (often different branches)
  Variant: Gshare (Scott McFarling’93): GA which takes logic OR of PC address bits and branch history bits
PA: Per address history, a > 0
  if a large almost each branch has a separate history
  so we correlate with same branch

## Slide 54: Accuracy, taking the best combination of parameters (a, k, m, n) :
Predictor Size (bytes)
64
128
Branch Prediction Accuracy (%)
256
1K
2K
4K
8K
16K
32K
64K
89
91
95
96
97
98
92
93
94
PA (10, 6, 4, 2)
GA (0,11,5,2)
Bimodal
GAs
PAs

## Slide 55: Branch Prediction; summary
Basic 2-bit predictor:
  For each branch:
    Predict taken or not taken
    If the prediction is wrong two consecutive times, change prediction
Correlating (global history) predictor:
  Multiple 2-bit predictors for each branch
  One for each possible combination of outcomes of preceding n branches
Local predictor:
  Multiple 2-bit predictors for each branch
  One for each possible combination of outcomes for the last n occurrences of this branch
Tournament predictor:
  Combine correlating global predictor with local predictor