## Slide 1: Embedded Computer Architecture 5SAI0 Instruction Level Parallel Architectures Part II
Henk Corporaal
www.ics.ele.tue.nl/~heco/courses/ECA
TUEindhoven
2021-2022

## Slide 2: Topics on ILP architectures
Introduction, Hazards (short recap)
Out-Of-Order (OoO) execution:
  Dependences limit ILP: dynamic scheduling
  Hardware speculation
Branch prediction (finish)
Multiple issue
How much ILP is there?
What can the compiler do?
Material Ch 3 (H&P or Dubois, second part)
But first … coming back on Tomasulo

## Slide 3: Speculation (Hardware based)
Execute instructions along predicted execution paths but only commit the results if the prediction was correct
Instruction commit: allowing an instruction to update the register file when instruction is no longer speculative
Need an additional piece of hardware to prevent any irrevocable action until an instruction commits:
  Reorder buffer, or Large renaming register file
  why? think about it?

## Slide 4: OoO execution with speculation using RoB
NEW

## Slide 5: Reorder Buffer (RoB)
RoB – holds the result of instruction between completion and commit
  Four fields per entry:
    Instruction type: branch/store/register
    Destination field: register number
    Value field: output value
    Ready field: completed execution? (is the data valid)
Modify reservation stations:
  Operand source-id is now RoB (if its producer is still in the RoB) instead of functional unit (check yourself!)

## Slide 6: Reorder buffer in operation
Book: H&P sect 3.6
# refers to reorder buffer entry

## Slide 7: Topics on ILP architectures
Introduction, Hazards (short recap)
Out-Of-Order (OoO) execution (H&P sect 3.4 - 3.6)
Branch prediction (H&P sect 3.3+3.9)
  1&2 bit prediction
  Branch correlation
  Avoiding branches: if-conversion
Multiple issue (H&P sect 3.7 – 3.8)
How much ILP is there?
What can the compiler do? (H&P sect 3.2)
Material Ch 3 (H&P or Dubois, second part)

## Slide 8: Branch Prediction
what is it?
why do we need it?
how does it work?
various schemes

## Slide 9: Branch Prediction Principles
breq r1, r2, label // if r1==r2 // then PCnext = label
// else PCnext = PC + 4 (for a RISC)
Questions:
do I jump ? -> branch prediction
where do I jump ? -> branch target prediction
what's the average branch penalty?
  <CPIbranch_penalty>
  i.e. how many instruction slots do I miss (or squash) due to branches

## Slide 10: Branch Prediction & Speculation
High branch penalties in pipelined processors:
  With about 20% of the instructions being a branch, the maximum ILP is five (but actually much less!)
CPI = CPIbase + fbranch * fmisspredict * cycles_penalty
  Large impact if:
    Penalty high: long pipeline
    CPIbase low: for multiple-issue processors,
Idea: predict the outcome of branches based on their history and execute instructions at the predicted branch target speculatively

## Slide 11: Branch Prediction Schemes
Predict branch direction:
1-bit Branch Prediction Buffer
2-bit Branch Prediction Buffer
Correlating Branch Prediction Buffer
Predicting next address:
Branch Target Buffer
Return Address Predictors
+ Or: try to get rid (some) of those malicious branches

## Slide 12: 1-bit Branch Prediction Buffer
1-bit branch prediction buffer or branch history table (BHT):
Buffer is like a cache without tags
Does not help for our MIPS pipeline because target address calculations performed in same stage as branch condition calculation
10…..10 101 00
0
1
0
1
0
1
1
0
PC
BHT
size=2k
k-bits

## Slide 13: Two 1-bit predictor problems
Aliasing: lower k bits of different branch instructions could be the same
  Solution: Use tags (the buffer becomes a tag); however very expensive
Loops are predicted wrong twice
  Solution: Use n-bit saturation counter prediction
    taken if counter  2 (n-1)
    not-taken if counter < 2 (n-1)
  A 2-bit saturating counter predicts a loop wrong only once
10…..10 101 00
0
1
0
1
0
1
1
0
PC
BHT
size=2k
k-bits

## Slide 14: 2-bit Branch Prediction Buffer
Solution: 2-bit scheme where prediction is changed only if mispredicted twice
Can be implemented as a saturating counter, e.g. as following state diagram:
T
T
NT
Predict Taken
Predict Not
Taken
Predict Taken
Predict Not
Taken
T
NT
T
NT
NT

## Slide 15: Next step: Correlating Branches
Fragment from SPEC92 benchmark eqntott:
if (aa==2)
aa = 0;
if (bb==2)
bb=0;
if (aa!=bb){..}
subi R3,R1,#2
b1: bnez R3,L1
add R1,R0,R0
L1: subi R3,R2,#2
b2: bnez R3,L2
add R2,R0,R0
L2: sub R3,R1,R2
b3: beqz R3,L3

## Slide 16: Correlating Branch Predictor
Idea: behavior of current branch is related to (taken/not taken) history of recently executed branches
  Then behavior of recent branches selects between, say, 4 predictions of next branch, updating just that prediction
(2,2) predictor: 2-bit global, 2-bit local
(k,n) predictor uses behavior of last k branches to choose from 2k predictors, each of which is n-bit predictor
  4 bits from branch address
2-bit global
branch history register
(01 = not taken, then taken)
2-bits per branch local predictors
Prediction
shift register,
remembers
last 2 branches

## Slide 17: Branch Correlation: the General Scheme
Table size (usually n = 2): Nbits = k * 2a + 2k * 2m *n
mostly n = 2
n-bit
saturating
Up/Down
Counter
Prediction
Branch Address
0
1
2k-1
0
1
2m-1
Branch History Table (BHT)
a
k
m
Pattern History Table
4 parameters: (a, k, m, n)

## Slide 18: Two varieties
GA: Global history, a = 0
  only one (global) history register  correlation is with previously executed branches (often different branches)
  Variant: Gshare (Scott McFarling’93): GA which takes logic OR of PC address bits and branch history bits
PA: Per address history, a > 0
  if a large almost each branch has a separate history
  so we correlate with the previous outcomes of the same branch

## Slide 19: Accuracy, taking the best combination of parameters (a, k, m, n) :
Predictor Size (bytes)
64
128
Branch Prediction Accuracy (%)
256
1K
2K
4K
8K
16K
32K
64K
89
91
95
96
97
98
92
93
94
PA (10, 6, 4, 2)
GA (0,11,5,2)
Bimodal
GAs
PAs

## Slide 20: Branch Prediction; summary
Basic 2-bit predictor:
  For each branch:
    Predict taken or not taken
    If the prediction is wrong two consecutive times, change prediction
Correlating (global history) predictor:
  Multiple 2-bit predictors for each branch
  One for each possible combination of outcomes of preceding n branches
Local predictor:
  Multiple 2-bit predictors for each branch
  One for each possible combination of outcomes for the last n occurrences of this branch
Tournament predictor:
  Combine correlating global predictor with local predictor

## Slide 21: Branch Prediction Performance

## Slide 22: Branch predition performance details for SPEC92 benchmarks
4096 Entries Unlimited Entries 1024 Entries
n = 2-bit BHT n = 2-bit BHT (a,k) = (2,2) BHT
0%
Mispredictions Rate
18%
Notes: As you see, using unlimited number of entries does not bring a big improvement w.r.t. 4 k entries (it just reduces the alias problem),
however, exploiting correlation is a big gain.

## Slide 23: Branch Prediction Accuracy
Mispredict because either:
  Wrong guess for that branch
  Got branch history of wrong branch when indexing the table (i.e. an alias occurred)
4096 entry table: misprediction rates vary from 1% (nasa7, tomcatv) to 18% (eqntott), with spice at 9% and gcc at 12%
For SPEC92, 4096 entries almost as good as infinite table
Real programs + OS are more like 'gcc'

## Slide 24: Branch Target Buffer
Predicting the Branch Condition is not enough !!
Where to jump? Branch Target Buffer (BTB):
  each entry contains a Tag and Target address
Tag branch PC
PC if taken
=?
Branch
prediction
(often in separate table)
Yes: instruction is branch. Use predicted PC as next PC if branch predicted taken.
No: instruction is not a
branch. Proceed normally
10…..10 101 00
PC

## Slide 25: Instruction Fetch Stage
Not shown: hardware needed when prediction was wrong
Instruction
Memory
PC
Instruction register
4
BTB
found & taken
target address

## Slide 26: Special Case: Return Addresses
Register indirect branches: hard to predict target address
  MIPS instruction: jr r3 // this means: PCnext = (r3)
    implementing switch/case statements
    FORTRAN computed GOTOs
    procedure return (mainly): jr r31 on MIPS
SPEC89: 85% of indirect branches used for procedure return
Since stack discipline for procedures, save return address in small buffer that acts like a stack:
  8 to 16 entries has already very high hit rate

## Slide 27: Return address prediction: example
main()
{ …
f();
…
}
f()
{ …
g()
…
}
100 main: ….
104 jal f
108 …
10C jr r31
120 f: …
124 jal g
128 …
12C jr r31
308 g: ….
30C
310 jr r31
314 ..etc..
main ra
return stack
108
128
Q: when does the return stack predict wrong?

## Slide 28: Or: ……..?? Avoid branches !

## Slide 29: Predicated Instructions (discussed before)
Avoid branch prediction by turning branches into conditional or predicated instructions:
If false, then neither store result nor cause exception
  Expanded ISA of Alpha, MIPS, PowerPC, SPARC have conditional move; PA-RISC can annul any following instr.
  IA-64/Itanium: conditional execution of any instruction
Examples:
  if (R1==0) R2 = R3; CMOVZ R2,R3,R1
  if (R1 < R2) SLT R9,R1,R2
  R3 = R1; CMOVNZ R3,R1,R9
  else CMOVZ R3,R2,R9
  R3 = R2;

## Slide 30: General guarding: if-conversion
if (a > b) { r = a % b; }
else { r = b % a; }
y = a*b;
sub t1,a,b
t1 rem r,a,b
!t1 rem r,b,a
mul y,a,b
sub t1,a,b
bgz t1,then
else: rem r,b,a
j next
then: rem r,a,b
next: mul y,a,b
CFG:
1
sub t1, a, b
bgz t1, 2, 3
4
mul y,a,b
…………..
3
rem r, b, a
goto 4
2
rem r, a, b
goto 4
Guards t1 & !t1
4 basic blocks
1 basic block
if-conversion

## Slide 31: Dynamic Branch Prediction: Summary
Prediction important part of scalar execution
Branch History Table: 2 bits for loop accuracy
Correlation: Recently executed branches correlated with next branch
  Either correlate with previous branches
  Or different executions of same branch
Branch Target Buffer: include branch target address (& prediction)
Return address stack for prediction of indirect jumps
Or….avoid branches: if-conversion

## Slide 32: Topics on ILP architectures
Introduction, Hazards (short recap)
Out-Of-Order (OoO) execution:
Branch prediction
Multiple issue
  Superscalar
  VLIW
  TTA (not in H&P)
How much ILP is there?
What can the compiler do?
Material Ch 3 (H&P or Dubois, second part)

## Slide 33: Going Parallel: Multiple Instructions Combined with OOO
Issue multiple instructions (or operations) per cycle

## Slide 34: Going parallel: Multiple Issue
Multiple parallel pipelines: CPI can get < 1
  complete multiple instructions per clock
Two Options:
  Statically scheduled superscalar processors
    VLIW (Very Long Instruction Word) processors
  Dynamically scheduled superscalar processors
    Superscalar processor
  EPIC (explicit parallel instruction computer)
    somewhat in between

## Slide 35: Multiple Issue Options:
Most used

## Slide 36: Modern Superscalar
Modern (superscalar) microarchitectures =
  Dynamic scheduling + Multiple Issue + Speculation
Issue logic can become bottleneck
  Several approaches:
    Assign reservation stations and update pipeline control table in half a clock cycle
      Only supports 2 instructions/clock
    Design logic to handle any possible dependencies between the instructions
    Hybrid approaches

## Slide 37: Multiple Issue: reduce complexity
Limit the number of instructions of a given class that can be issued in a “bundle”
  I.e. one FloatingPt, one Integer, one Load, one Store
Examine all the dependencies among the instructions in the bundle
If dependencies exist in bundle, encode them in reservation stations
Need multiple completions&commits per cycle

## Slide 38: Example: increment array elements
Loop: LD R2, 0(R1) ;R2=array element
DADDIU R2, R2,#1 ;increment R2
SD R2, 0(R1) ;store result
DADDIU R1, R1, #8 ;increment R1 to point to next double
BNE R2, R3, Loop ;branch if not final iteration

## Slide 39: Example (No Speculation)
Note: LD following BNE must wait on the branch outcome (no speculation)!

## Slide 40: Example (with branch Speculation)
Note: Execution of 2nd DADDIU is earlier than 1th, but commits later, i.e. in order!

## Slide 41: Nehalem microarchitecture (Intel)
first use: Core i7
  2008
  45 nm
hyperthreading
shared L3 cache
3 channel DDR3 controler
QIP: quick path interconnect
32K+32K L1 per core
256 L2 per core
4-8 MB L3 shared between cores

## Slide 42: Limitations of OoO Superscalar
Available ILP is limited
  usually we’re not programming with parallelism in mind
Huge hardware cost when increasing issue width
  adding more functional units is easy, however:
  more memory ports and register ports needed
  dependency check needs O(n2) comparisons
  renaming needed
  complex issue logic (check and select ready operations)
  complex forwarding circuitry
Any cheaper alternatives ???

## Slide 43: VLIW: alternative to Superscalar
Hardware much simpler!! Why??
Limitations of VLIW processors
  Very smart compiler needed (but largely solved!)
  Loop unrolling helps but increases code size
  Unfilled slots waste instruction bits (need NOPs)
  Cache miss stalls whole pipeline
    Research topic: scheduling loads
  Binary incompatibility
    (.. can partly be solved: EPIC or JITC .. )
  Note:
    Still many ports on register file needed
    Complex forwarding circuitry and many bypass buses
      Solve these issues later

## Slide 44: Single Issue RISC vs Superscalar
op
op
op
op
op
op
op
op
op
op
op
op
execute
1 instr/cycle
instr
instr
instr
instr
instr
instr
instr
instr
instr
instr
instr
instr
(1-issue)
RISC CPU
Change HW,
but can use
same code
op
op
op
op
op
op
op
op
op
op
op
op
issue and (try to) execute
3 instr/cycle
instr
instr
instr
instr
instr
instr
instr
instr
instr
instr
instr
instr
3-issue Superscalar

## Slide 45: Single Issue RISC vs VLIW
Compiler
op
op
op
nop
op
op
op
op
nop
op
nop
op
op
op
op
instr
instr
instr
instr
instr
op
op
op
op
op
op
op
op
op
op
op
op
execute
1 instr/cycle
instr
instr
instr
instr
instr
instr
instr
instr
instr
instr
instr
instr
RISC CPU
3-issue VLIW
execute
1 instr/cycle
3 ops/cycle

## Slide 46: VLIW: general concept
A VLIW architecture with 7 FUs
Int Register File
Instruction Memory
Int FU
Data Memory
Int FU
Int FU
LD/ST
LD/ST
FP FU
Floating Point
Register File
FP FU
Instruction register
Function
units

## Slide 47: VLIW characteristics
Multiple operations per instruction
One instruction per cycle issued (at most)
Compiler is in control
Only RISC like operation support
  Short cycle times
  Easier to compile for
Flexible: Can implement any FU mixture
Extensible / Scalable
However:
tight inter FU connectivity required
not binary compatible !!
  (new long instruction format)
low code density
add
sub
sll
nop
bne
Example VLIW instructions

## Slide 48: VelociTIC6x datapath

## Slide 49: VLIW example: TMS320C62
TMS320C62 VelociTI Processor
8 operations (of 32-bit) per instruction (256 bit)
Two clusters
  8 Fus: 4 Fus / cluster : (2 Multipliers, 6 ALUs)
  2 x 32 registers
  One bus available to write in register file of other cluster
Flexible addressing modes (like circular addressing)
Flexible instruction packing
All instruction conditional
Originally: 5 ns, 200 MHz, 0.25 um, 5-layer CMOS
128 KB on-chip RAM

## Slide 50: VLIW example: Philips TriMedia TM1000
Exec
unit
Exec
unit
Exec
unit
Exec
unit
Exec
unit
Register file (128 regs, 32 bit, 15 ports)
Instruction register (5 issue slots)
Data
cache
(16 kB)
PC
Instruction
cache (32kB)
5 constant
5 ALU
2 memory
2 shift
2 DSP-ALU
2 DSP-mul
3 branch
2 FP ALU
2 Int/FP ALU
1 FP compare
1 FP div/sqrt

## Slide 51: Summary (so far) on ILP architectures
Superscalar
  Binary compatible
  Multi-issue, OoO, branch speculation
VLIW
  Not binary compatible, requires re-compilation of source code
  More energy efficient
ILP architectures to be discussed in part III:
  EPIC
  TTA