## Slide 1: Embedded Computer Architecture 5SAI0 Exploiting Data Reuse: Loop Transformations
Patrick Wijnings
Original slides by Henk Corporaal
www.ics.ele.tue.nl/~heco/courses/ECA
h.corporaal@tue.nl p.w.a.wijnings@tue.nl
TU/e 2021-2022

## Slide 2: GoogLeNet: Energy
Yang.e.a CVPR'17
CNN layers: 21 depth, 57 in total
FC layer: 1
Weights: 7.0 M
MACs: 1.43 G per input

## Slide 3: Where is the energy going

## Slide 4: VGG16 example
Conv layers: 13
FC Layers: 3
Weights: 138 M
MACs: 15.5 G per input
Simonyan, ICLR 2015

## Slide 5: Reducing external memory accesses
Original code
Rescheduled code
VGG16 example
Conclusion: we need advanced loop transformation to
exploit data locality (in local buffers), reducing external accesses

## Slide 6: Overview loop transformations
Motivation
Data flow transformations
Loop scheduling transformations: iteration reordering
Loop restructuring
Material
  partly in H&P: 4.5
  GPU lab material (online)

## Slide 7: Application Excecution Time
High performance computing
Embedded computing
Small portions of the code dominate execution time
  Hot spots
  Loops
Apply Loop Transformations
for(i=0; i<N; i++){
for(j=0; j<N; j++){
for(k=0; k<N; k++)
c[i][j] += a[i][k] * b[k][j];
}}

## Slide 8: Loop Transformations
Can help you in many compute domains
CPU Code
Parallelism
Memory Hierarchy
Convert Loops to
GPU Threads
Embedded Devices
Fine-tune for architecture
HDL (HW Description Languages)

## Slide 9: Data flow transformations

## Slide 10: Data flow transformation: Loop-Based Strength Reduction
Replace an expensive operation
Can be multiplication, especially for embedded cores
No HW multiplier, e.g. MicroBlaze
An optimizing compiler can help
c=3;
for(i=0; i<N; i++){
a[i] = a[i] + i*c;
}
c=3;
T=0;
for(i=0; i<N; i++){
a[i] = a[i] + T;
T = T + c;
}
* Examples are from: D.F. Bacon, S.L. Graham, and O.J. Sharp, Compiler transformations for high-performance computing. ACM Comput. Surv. 26, (1994)

## Slide 11: Data flow transformation: Induction Variable Elimination
Induction variable?
  Compute loop exit conditions
  Compute memory addresses
Given a known final value and relation to addresses
  Possible to eliminate index calculations
Again an optimizing compiler can help
A = &a[0];
T = &a[0] + N;
while(A<T){
*A = *A + c;
A++;
}
for(i=0; i<N; i++){
a[i] = a[i] + c;
}
Notes: Performing the control of a loop is basically overhead. I refer to the increment of i and the compare of i<N to check if the exit condition is not met.
With induction variable elimination we can reduce this overhead.

## Slide 12: Data flow transformation: Loop-Invariant Code Motion
Index of c[] does not change
Move one loop up and store in register
Reuse it over iterations of inner loop
Most compilers can perform this
Example is similar to Scalar Replacement Transformation
for(i=0; i<N; i++){
for(j=0; j<N; j++){
a[i][j]=b[j][i]+c[i];
}
}
for(i=0; i<N; i++){
T=c[i];
for(j=0; j<N; j++){
a[i][j]=b[j][i]+T;
}
}

## Slide 13: Data flow transformation: Loop Unswitching
Conditional execution in body
Speculative branch prediction helps but
This branch is loop invariant code
  Move it outside the loop
  Each execution path independent loops
Increases code size
for(i=0; i<N; i++){
a[i] = b[i];
if(x<7){a[i]+=5;}
}
if(x<7){
for(i=0; i<N; i++){
a[i]=b[i];
a[i]+=5;
}
}
else{
for(i=0; i<N; i++){
a[i]=b[i];
}
}

## Slide 14: Iteration reordering

## Slide 15: Loop representation as Iteration Space
for(i=0; i<N; i++){
for(j=0; j<N; j++){
A[i][j] = B[j+3][i+2];
Each position represents an iteration
  At each position 1 or more array elements are accessed

## Slide 16: Visitation order in Iteration Space
for(i=0; i<N; i++){
for(j=0; j<N; j++){
A[i][j] = B[j+3][i+2];
Iteration space is not data space
for(j=0; j<N; j++){
for(i=0; i<N; i++){
A[i][j] = B[j+3][i+2];

## Slide 17: But we don’t have to be regular
A[i][j] = B[j+3][i+2];
But order can have huge impact on:
  Memory Hierarchy
    E.g. Reuse of data (improve locality)
  Parallelism
  Loop or control overhead

## Slide 18: Iteration Reordering Transformations
Change the relative ordering
  Improve locality by matching with a memory hierarchy
  Expose parallelism by altering iteration dependencies
  Reduce loop or control overhead
We need more theory to understand these
Or combine the tricks to form a methodology
Normal compilers often don’t help you with this
Only state-of-the-art (research) compilers can help
*Based on:
M. Wolf, M. Lam, A Data Locality Optimizing Algorithm. ACM SIGPLAN, PLDI (1991)

## Slide 19: Loop Interchange or Loop Permutation
for(i=0; i<N; i++){ for(j=0; j<N; j++){
for(j=0; j<N; j++){ for(i=0; i<N; i++){
A[j][i] = i*j; A[j][i] = i*j;
N is large with respect to cache size
Normal compilers will not help you!
Chart: Execution Time [ms]
| -O0 | -O3
Without | 809.7 | 385
With | 545.3 | 77
Notes: Example to demonstrate the possible locality increase due to interchange

## Slide 20: Loop Interchange or Loop Permutation
for(i=0; i<N; i++){ for(j=0; j<N; j++){
for(j=0; j<N; j++){ for(i=0; i<N; i++){
A[j][i] = i*j; A[j][i] = i*j;
Assumptions:
1. Memory layout row major
2.Cache line size=4 elements
Notes: Example to demonstrate the possible locality increase due to interchange

## Slide 21: Types of data reuse
for i := 0 to 2
for j := 0 to 100
A[i][j] = B[j+1][0] + B[j][0];
Notes: Spatial reuse = reuse of neighboring values in cache lines; Temporal reuse = Single value reused at different moment in time;
Group reuse = multiple memory references in the loop body point to the same memory location at different iteration values (temporal) or they point to neighboring values (spatial)

## Slide 22: Optimize array accesses for memory hierarchy
Solve the following questions?
  When do misses occur?
    Use “locality analysis”
  Is it possible to change iteration order to produce better behavior?
    Evaluate the cost of various alternatives
  Does the new ordering produce correct results?
    Use “dependence analysis”
Notes: Introduce theory for memory hierarchy optimization

## Slide 23: Different Reordering Transformations
Loop Interchange
Tiling
Loop Reversal
Skewing
Can improve locality
Can enable above

## Slide 24: Tiling the Iteration Order
Result in Iteration Space
for(jj=0; jj<N; jj+=Tj){
for(i=0; i<N; i++){ for(i=0; i<N; i++){
for(j=0; j<N; j++){ for(j=jj; j<jj+Tj; j++){
f(A[i],A[j]); f(A[i],A[j]);
assume
Tj=4
Notes: Example to show the potential locality increase due to tiling

## Slide 25: Cache Effects of Tiling
for(jj=0; jj<N; jj+=Tj){
for(i=0; i<N; i++){ for(i=0; i<N; i++){
for(j=0; j<N; j++){ for(j=jj; j<jj+Tj; j++){
f(A[i],A[j]); f(A[i],A[j]);
assume Tj=4
Iteration
space (i,j)
Again, assume N >> cache size - A does not fit in the cache

## Slide 26: Is this always possible?
No, dependencies can prevent transformations
Interchange and Tiling is not always valid!
Example Interchange
  Spatial locality
  Dependency (1,-1)
Should be lexicographically correct
for(i=1; i<N; i++){
for(j=0; j<N; j++){
a[j][i] = a[j+1][i-1] + 1;
}
}
Dependence vectors

## Slide 27: Lexicographical ordering
Each iteration is a node identified by its n-dim. index vector: p = (p1, p2, …, pn)
Iterations are executed in lexicographic order
For p = (p1, p2, …, pn) and q = (q1, q2, …, qn) p is lexicographically greater than q written as p q
  Therefore iteration p must be executed after q
Example:
    (1,1,1), (1,1,2), (1,1,3), …,
    (1,2,1), (1,2,2), (1,2,3), …,
    …,
    (2,1,1), (2,1,2), (2,1,3), …,
  (1,2,1) (1,1,2) ? (1,4,2) (2,1,1) ?
A little quiz?
Notes: Lexicographical ordering introduced this will be used during the dependency analysis later on.

## Slide 28: Dependence vectors
Dependence vector in an n-nested loop is denoted as a vector: d = (d1, d2, …, dn)
A single dependence vector represents a set of distance vectors
A distance vector defines a distance in the iteration space
Distance vector is difference between target and source iterations:
  d = IT – IS
Notes: Dependence distance introduced. Not always possible can also be a direction vector.

## Slide 29: Example of dependence vector
For(i=0; i<N; i++){
for(j=0; j<N; j++)
A[i,j] = …;
= A[i,j];
B[i,j+1] = …;
= B[i,j];
C[i+1,j] = …;
= C[i,j+1];
A yields: B yields: C yields:
A0,0= =A0,0
B0,1= =B0,0
C1,0= =C0,1
A0,1= =A0,1
B0,2= =B0,1
C1,1= =C0,2
A1,0= =A1,0
B1,1= =B1,0
C2,0= =C1,1
A1,1= =A1,1
B1,2= =B1,1
C2,1= =C1,2
A0,2= =A0,2
B0,3= =B0,2
C1,2= =C0,3
A1,2= =A1,2
B1,3= =B1,2
C2,2= =C1,3
A2,0= =A2,0
B2,1= =B2,0
C3,0= =C2,1
A2,1= =A2,1
B2,2= =B2,1
C3,1= =C2,2
A2,2= =A2,2
B2,3= =B2,2
C3,2= =C2,3
i
j

## Slide 30: Plausible dependence vectors
A dependence vector is plausible iff it is lexicographically non-negative
For(i=0; i<N; i++){
for(j=0; j<N; j++)
.......
Plausible: (1,-1)
Implausible: (-1,0)

## Slide 31: Loop Reversal
  Dependency (1,-1) Dependency (1,1)
loop interchange is valid after loop reversal
for(i=0; i<N; i++){
for(j=0; j<N; j++){
a[j][i] = a[j+1][i-1] + 1;
}
}
for(i=0; i<N; i++){
for(j=N-1; j>=0; j--){
a[j][i] = a[j+1][i-1] + 1;
}
}

## Slide 32: More difficult example
For(i=0; i<6; i++){ D={(0,1),(1,0),(1,-1)}
for(j=0; j<7; j++){
A[j+1] += 1/3 * (A[j] + A[j+1] + A[j+2]);
What are other legal visit orders?

## Slide 33: Loop Skewing
for(i=0 i<6; i++){ D = {(0,1),(1,0),(1,-1)}
for(j=0; j<7; j++){
A[j+1] = 1/3 * (A[j] + A[j+1] + A[j+2]);
for(i=0; i<6; i++){ D = {(0,1),(1,1),(1,0)}
for(j=i; j<7+i; j++){
A[j-i+1] = 1/3 * (A[j-i] + A[j-i+1] + A[j-i+2]);
Notes: Original dependence vector top vs dependence vector bottom

## Slide 34: Loop skewing enables Tiling
Apply Skew Transformation
Apply Tiling

## Slide 35: Is It Really That Easy ?
No, we forget a few things
Cache capacity and reuse distance
  If caches were infinitely large, we would be finished
For deep loopnests analysis can be very difficult
It would be much better to automate these steps
We need more theory and tools
Cost models

## Slide 36: Data Reuse distance
The number of unique accesses between a use and a reuse is defined as the (data) reuse distance:
( a[0] a[6] a[20] b[1] a[6] a[0] ) => RD (a[0])= 3
* C. Ding, Y. Zhong, Predicting Whole-Program Locality through Reuse Distance Analysis, PLDI (2003)
Second a[0] access is a cache hit if
  Fully associative cache with n=4 entries
  Optimal LRU, least recently used, replacement policy
In general:
  Cache hit if RD < n
  Cache miss if RD ≥ n
We can measure reuse distance with profiling tools:
  Suggestions for Locality Optimization (SLO)
Beyls, K., D'Hollander, E. Refactoring for Data Locality, IEEE Computer Vol. 42, no. 2 2009
Notes: Can be line adresses

## Slide 37: Study a matrix multiplication kernel
Loop interchange
for(i=0; i<Bi; i++){
for(j=0; j<Bj; j++){
for(k=0; k<Bk; k++){
C[i][j] += A[i][k] * B[k][j];
for(j=0; j<Bj; j++){
for(k=0; k<Bk; k++){
for(i=0; i<Bi; i++){
C[i][j] += A[i][k] * B[k][j];

## Slide 38: Loop tiling
Can be done in multiple dimensions
Manual exploration is intractable
for(i=0; i<Bi; i++){
for(j=0; j<Bj; j++){
for(k=0; k<Bk; k++){
C[i][j] += A[i][k] * B[k][j];
for(i=0; i<Bi; i++){
for(jj=0; jj<Bj; jj+=Tj){
for(k=0; k<Bk; k++){
for(j=jj; j<jj+Tj; j++)
C[i][j] += A[i][k] * B[k][j];

## Slide 39: LOOP RESTRUCTURING

## Slide 40: Loop Unrolling
Duplicate loop body and adjust loop header
  Increases ILP (Instruction Level Parallelism)
  Reduces loop overhead (fewer branches and counter increments)
  Possibilities for common subexpression elimination
If partial unroll, loop should stay in original bound!
Downsides
  Code size increases, can increase I-cache miss-rate
for(i=1; i<N; i++){
a[i]=a[i-1]+a[i]+a[i+1];
}
for(i=1; i<N-1; i+=2){
a[i]=a[i-1]+a[i]+a[i+1];
a[i+1]=a[i]+a[i+1]+a[i+2];
}
if(mod(N-1,2)==1){
a[N-1]=a[N-2]+a[N-1]+a[N];

## Slide 41: Loop Merge or Fusion
Why?
  Improve locality
  Reduce loop overhead
for(i=0; i<N; i++){
b[i]=a[i]+1;
}
for(j=0; j<N; j++){
c[j]=b[j]+a[j];
}
for(i=0; i<N; i++){
b[i]=a[i]+1;
c[i]=b[i]+a[i];
}
Location
Time
Production/Consumption
Consumption(s)
Location
Time
Production/Consumption
Consumption(s)

## Slide 42: Fusion is not always allowed
Data dependencies from first to second loop
Fusion is allowed if
   I: cons(I) in loop 2  prod(I) in loop 1
Enabling transformations: Bump, Reverse, Skew
for(i=0; i<N; i++){
b[i]=a[i]+1;
}
N-1>=i
for(i=0; i<N; i++){
c[i]=b[N-1]+a[i];
}
for(i=0; i<N; i++){
b[i]=a[i]+1;
}
i-2 < i
for(i=0; i<N; i++){
c[i]=b[i-2]+a[i];
}

## Slide 43: Loop Bump: Example as enabler
for(i=2; i<N; i++){
b[i]=a[i]+1;
}
for(i=2; i<N; i++){
c[i-2]=b[i+2-2]*0.5;
}
for(i=2; i<N; i++){
b[i]=a[i]+1;
}
for(i=0; i<N-2; i++){
c[i]=b[i+2]*0.5;
}
for(i=2; i<N; i++){
b[i]=a[i]+1;
c[i-2]=b[i]*0.5;
}
i+2 > i => direct merging not possible
i+2-2 = i => possible to merge

## Slide 44: Main Take-Aways
Data-Flow-Based Transformations
  Good compilers can help
Iteration Reordering Transformations
  High-level transformations
  Compilers are often not enough
  Huge gains for parallelims and locality
  Be carefull with dependencies
Loop Restructuring Transformations
  Similar to reordering

## Slide 45: Extra Enabler Transformations
Many of these can be very useful
Especially to enable the beneficial ones:
  Interchange
  Tiling
  Fusion
Often you need combinations to get the job done!
Try to use them all in the assignments!