## Slide 1: Embedded Computer Architecture 5SAI0 Memory Hierarchy Part I
Henk Corporaal
www.ics.ele.tue.nl/~heco/courses/ECA
h.corporaal@tue.nl
TUEindhoven
2021-2022

## Slide 2: Topics Memory Hierarchy Part I
Memory hierarchy motivation
Caches
  direct mapped
  set-associative
Basic cache optimizations
Part II (Dec 1)
  Advanced cache optimizations
  Memory design
  Virtual memory
    Address mapping and Page tables, TLB
=> Material book: Ch2 + App B (H&P) / Ch 4 (Dubois)
But first: Other Architecture Styles

## Slide 3: Remember RISC? Keep it simple
RISC characteristics:
Reduced number of instructions
Limited number of instruction sizes (preferably one)
  know directly where the following instruction starts
Limited number of instruction formats
Limited addressing modes
  load-store architecture
  enables pipelining
Large register set
  uniform (no distinction between e.g. address and data registers)
Memory alignment restrictions
Pipelined implementation

## Slide 4: Other architecture styles
Accumulator architecture
  one operand (in register or memory), accumulator almost always implicitly used
Stack
  zero operand: all operands implicit (on TOS)
Register (load store) = RISC
  three operands, all in registers
  loads and stores are the only instructions accessing memory (i.e. with a memory (indirect) addressing mode
Register-Memory
  two operands, one in memory
Memory-Memory
  three operands, may be all in memory
(there are more varieties / combinations)

## Slide 5: Accumulator Architecture
Accumulator
ALU
Memory
registers
address
latch
latch
Example code: a = b+c;
load b; // accumulator is implicit operand
add c;
store a;

## Slide 6: Stack Architecture
ALU
Memory
top of
stack
stack pt
latch
latch
latch
Example code: a = b+c;
push b;
push c;
add;
pop a;
b
b
c
b+c
push b
push c
add
pop a
stack:

## Slide 7: Other architecture styles
Stack Architecture | Accumulator Architecture | Register-Memory | Memory-Memory | Register (load-store)
Push A | Load A | Load r1,A | Add C,B,A | Load r1,A
Push B | Add B | Add r1,B |  | Load r2,B
Add | Store C | Store C,r1 |  | Add r3,r1,r2
Pop C |  |  |  | Store C,r3
Let's look at the code for C = A + B
Note: in code A stands for (r) where register r contains &a; similar for B,C
Q: What are the advantages / disadvantages of load-store (RISC) architecture?
RISC
Notes: Pros:
• Small set of instructions: easier for compilers to produce more efficient codes.
• A single instruction takes one cycle.
• Fixed length of instruction, few parameters, easier to pipeline.
• Fewer instruction formats, a lesser number of instructions, and fewer addressing modes.
• Decoding logic is simple.
• More general-purpose registers. Shorter time for loading.
• Smaller area chip.
• More energy-efficient than CISC.
Cons:
• Performance depends on compiler/programmer.
• Compiler needs to decompose high-level instructions into many simple ones.
• Increased the code size.
• Large memory caches.

## Slide 8: Many addressing modes; RISC uses only 3-4
MODE | EXAMPLE | MEANING
REGISTER | ADD R4, R3 | reg[R4] <- reg[R4] +reg[R3]
IMMEDIATE | ADD R4, #3 | reg[R4] <- reg[R4] + 3
DISPLACEMENT | ADD R4, 100(R1) | reg[R4] <- reg[R4] + Mem[100 + reg[R1]]
REGISTER INDIRECT | ADD R4, (R1) | reg[R4] <- reg[R4] + Mem[reg[R1]]
INDEXED | ADD R3, (R1+R2) | reg[R3] <- reg[R3] + Mem[reg[R1] + reg[R2]]
DIRECT OR ABSOLUTE | ADD R1, (1001) | reg[R1] <- reg[R1] + Mem[1001]
MEMORY INDIRECT | ADD R1, @R3 | reg[R1] <- reg[R1] + Mem[Mem[Reg[3]]]
POST INCREMENT | ADD R1, (R2)+ | ADD R1, (R2) then R2 <- R2+d
PREDECREMENT | ADD R1, -(R2) | R2 <- R2-d then ADD R1, (R2)
PC-RELATIVE | BEZ R1, 100 | if R1==0, PC <- PC+100
PC-RELATIVE | JUMP 200 | Concatenate bits of PC and offset

## Slide 9: Topics Memory Hierarchy Part I
Memory hierarchy motivation
Caches
  direct mapped
  set-associative
Basic cache optimizations
  Classification of cache misses: the 3 C’s
=> Material book: Ch2 + App B (H&P) / Ch 4 (Dubois)

## Slide 10: Memory Performance Gap single processor performance vs memory latency
Huge performance gap between CPU and Memory

## Slide 11: Memory Hierarchy

## Slide 12: Memory Hierarchy Design
Very crucial with recent multi-core processors:
  Aggregate peak bandwidth grows with # cores !
Example:
  Intel Core i7 can generate two references per core per clock
  With 4 cores and 3.2 GHz clock =>
    25.6 billion 64-bit data references/second +
    12.8 billion 128-bit instruction references
    = 409.6 GB/s!
  DRAM bandwidth is only 6% of this (25 GB/s)
  We need:
    Multi-port, pipelined caches
    Two levels of cache per core
    Shared (between cores) third-level (L3) cache on chip
Microprocessors have >> MB on-chip cache; huge area
Memory and caches consume much energy

## Slide 13: Why does a (small) cache work?
Your program and data sizes >> cache size ??
LOCALITY !!!!!
  Temporal: you are likely accessing the same address soon again
  Spatial: you are likely accessing another address close to the current one in the near future

## Slide 14: Topics Memory Hierarchy Part I
Memory hierarchy motivation
Caches
  direct mapped
  set-associative
Basic cache optimizations
  Classification of cache misses: the 3 C’s
=> Material book: Ch2 + App B (H&P) / Ch 4 (Dubois)

## Slide 15: Cache operation
Memory / Lower level
Cache / Higher level
block / line
tags
data

## Slide 16: Direct Mapped Cache
Mapping: block address modulo the number of blocks in the cache

## Slide 17: Direct Mapped Cache
Q:What kind of locality are we taking advantage of?
2
0
1
0
B
y
t
e
o
f
f
s
e
t
V
a
l
i
d
T
a
g
D
a
t
a
I
n
d
e
x
0
1
2
1
0
2
1
1
0
2
2
1
0
2
3
T
a
g
I
n
d
e
x
H
i
t
D
a
t
a
2
0
3
2
3
1
3
0
1
3
1
2
1
1
2
1
0
Address (bit positions)

## Slide 18: Direct Mapped Cache
Taking advantage of spatial locality:
Address (bit positions)

## Slide 19: Memory hierarchy basics
When a word is not found in the cache, a miss occurs:
  Fetch word from lower level in hierarchy, requiring a higher latency reference
  Lower level may be another cache or the main memory
  Also fetch the other words contained within the block
    Takes advantage of spatial locality
    Often costs extra cycles delay
  Place block into cache in any location within its set, determined by address
    block address MOD number of sets in cache

## Slide 20: Cache basics
Set 1
Way 3
4-ways set-associative cache (Nsets =4): each set contains 4 blocks

## Slide 21: Cache basics
cache_size = Nsets * Assoc * Block_size
block_address = Byte_address DIV Block_size (in bytes)
index = Block_address MOD Nsets
Because the block size and Nsets are (usually) powers of two, DIV and MOD can be performed efficiently; how?
tag
index
block
offset
block address
… 2 1 0
31 …

## Slide 22: Cache performance: metrics & terminology
Average memory access time (AMAT)
AMAT= hit_time + miss_rate * miss_penalty
Miss rate: fraction of accesses not satisfied by the cache (at a certain level Li)
  Number of misses is divided by the number of processor references
  Also hit_rate = 1 – miss_rate
Miss_penalty: average delay per miss caused in the processor
  If processor blocks on misses, then this is simply the number of clock cycles to bring a block from memory, also called miss latency
  In a OoO (Out-of-Order) processor, the penalty of a miss cannot be measured directly
  Different from miss latency
Miss rate and penalty can be defined for all cache levels Li

## Slide 23: Cache performance: metrics&terminology
Misses per instructions (MPI)
  Number of misses in Level_i (Li) divided by number of instructions
  Easier to use than miss rate: CPI = CPI0 + MPI*miss_penalty
Note: speculative and multithreaded processors may execute other instructions during a miss
  Reduces performance impact of misses

## Slide 24: 4 questions for designers
Q1: Where can a block be placed in the upper level? (Block placement)
  Fully Associative, Set Associative, Direct Mapped
Q2: How is a block found if it is in the upper level? (Block identification)
  Tag/Block
Q3: Which block should be replaced on a miss? (Block replacement)
  Random, FIFO (First-in First-out), LRU (Least Recently Used)
Q4: What happens on a write? (Write strategy)
  Write Back or Write Through (with Write Buffer)

## Slide 25: Write policies
Write through: write to next level on all writes
  Combined with write buffer to avoid CPU stalls
  Simple, no inconsistency among levels
Write-back: write to next level only on replacement
    With the help of a dirty bit and a write-back buffer
  Writes happen on a miss only
Allocation on write miss
  Always allocate in write-back; design choice in write-through

## Slide 26: Topics Memory Hierarchy Part I
Memory hierarchy motivation
Caches
  direct mapped
  set-associative
Basic cache optimizations
  Classification of cache misses: the 3 C’s
=> Material book: Ch2 + App B (H&P) / Ch 4 (Dubois)

## Slide 27: Basic Cache optimizations
Larger cache capacity to reduce miss rate
  Increases hit time, increases power consumption
Larger block size
  Reduces compulsory misses (by exploiting more spatial locality)
  Increases capacity and conflict misses, increases miss penalty
Higher associativity
  Reduces conflict misses
  Increases hit time, increases power consumption
More cache levels
  Reduces overall memory access time
Split L1 data and L1 instruction cache
  can access data and instructions in parallel, even for single ported caches

## Slide 28: Effect of cache parameters
Larger caches
  Slower, more complex, more energy/access, but fewer capacity misses
Larger block size
  Exploit more spatial locality
  However: Too big a block increases capacity misses
  Big blocks also increase miss penalty (takes much more time to load a line from next level
Higher associativity
  Addresses conflict misses
  However: higher hit time, more energy/access
  8-16 way SA (Set-Associative) is as good as Fully Associative

## Slide 29: Cache mapping
Direct-mapped: each memory block can be mapped to only one cache line:
  cache index = block address modulo the number of lines in cache
Set-associative: each memory block can be mapped to a set of lines in cache;
  set number = block address modulo the number of cache sets
Fully associative: each memory block can be in any cache line
  effectively there is only one set
Notes: Memory blocks are mapped to cache lines
  Mapping can be direct, set-associative or fully associative

## Slide 30: Direct Mapped Cache: Problem !?!
Many memory addresses map to the same cache line
=> Conflicts
Solution:
  Associative caches

## Slide 31: A 4-Way Set-Associative Cache
Set 1
Way 3
4-ways: Each set contains 4 blocks
Fully associative cache has only 1 set, containing all blocks

## Slide 32: Replacement policies
Random, LRU, FIFO, pseudo-LRU
Example: least-recently used (LRU)
  replacement priority per cache line (11 = should be replaced)
Notes: Numbers indicate replacement priority, highest = 11. Higher means closer to replacement. So priority 0 = MRU (most recently used) line.
line 3 gets lowest replacement priority = 00. all entries below the original priority of line 3 (was 10) get incremented.
miss => replace line 2 => its priority is set to 00, all others are incremented.

## Slide 33: LRU Visualised
Most Recently Used (MRU)
Line 3 - 10
Line 2 - 11
Line 0 - 01
Line 1 - 00
Least Recently Used (LRU)
Priority level == index in this stack

## Slide 34: LRU Visualised
Most Recently Used
Line 3 - 10
Line 2 - 11
Line 0 - 01
Line 1 - 00
Least Recently Used
Hit on line 3
Hit on Line 3

## Slide 35: LRU Visualised
Most Recently Used
Line 3 - 10
Line 2 - 11
Line 0 - 01
Line 1 - 00
Least Recently Used
Hit on line 3
Line 3 needs to become MRU

## Slide 36
Most Recently Used
Line 3 - 10
Line 2 - 11
Line 0 - 01
Line 1 - 00
Least Recently Used
Hit on line 3
Move line 3 to top
Indexes need fixing!

## Slide 37
Most Recently Used
Line 3 - 00
Line 2 - 11
Line 0 - 01
Line 1 - 00
Least Recently Used
Hit on line 3
line 3 gets index 00

## Slide 38
Most Recently Used
Line 3 - 00
Line 2 - 11
Line 0 - 01
Line 1 - 00
Least Recently Used
Hit on line 3
+1
Every line with index lower than old index of line 3 is incremented

## Slide 39
Most Recently Used
Line 3 - 00
Line 2 - 11
Line 0 - 10
Line 1 - 01
Least Recently Used
Hit on line 3
+1
Every line with index lower than old index of line 3 is incremented

## Slide 40: LRU Visualised
Most Recently Used
Line 3 - 00
Line 2 - 11
Line 0 - 10
Line 1 - 01
Least Recently Used
All indexes are up to date

## Slide 41: LRU Index Update Hardware
Most Recently Used
Line 3 - 00
Line 2 - 11
Line 0 - 10
Line 1 - 01
Least Recently Used
index = hit ? 00 : ( index<hit_index) ? index+1 : index

## Slide 42: LRU Index Update Hardware
Most Recently Used
Line 3 - 00
Line 2 - 11
Line 0 - 10
Line 1 - 01
Least Recently Used
index = hit ? 00 : ( index<hit_index) ? index+1 : index
Mux
Sub+Comp
Mux
Incr.
Mux

## Slide 43: LRU Index Update Hardware
Most Recently Used
Line 3 - 00
Line 2 - 11
Line 0 - 10
Line 1 - 01
Least Recently Used
index = hit ? 00 : ( index<hit_index) ? index+1 : index
Mux
Sub+Comp
Mux
Incr.
Mux
For each way!!

## Slide 44: Multilevel Caches
Primary, level-1 cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Some high-end systems include L-3 cache
In that case, main memory services L-3 cache misses
CPU
L1 $
L2 $
Main Memory
L3 $

## Slide 45: The cache/memory performance equation
Texec = Ncycles • Tcycle = Ninst• CPI • Tcycle
with
CPI = CPIideal + CPIstall
CPIstall = %reads • missrateread • misspenaltyread +
%writes • missratewrite • misspenaltywrite
or:
Texec = (Nnormal-cycles + Nstall-cycles ) • Tcycle
with
Nstall-cycles = Nreads • missrateread • misspenaltyread +
Nwrites • missratewrite • misspenaltywrite
(+ Write-buffer stalls )
Note: 1) often reads and writes are combined
2) often Instructions and Data are taken separately

## Slide 46: Multilevel Cache: calculate CPI?
Let’s first look at a 1-level cache:
  CPU with CPIbase = 1, clock rate = 4GHz
  Miss rate/instruction = 2%
  Main memory access time = 100ns
What is the CPI with only a L1 cache?
Miss penalty = 100ns/0.25ns = 400 cycles
CPI = CPIbase + miss_rate * miss_penalty = 1 + 0.02 × 400 = 9 cycles/instruction
CPU
L1 $
Main Memory

## Slide 47: Example (cont.)
Now add L2 cache
  Access time = 5ns
  Global miss rate to main memory = 0.5%
L1 miss with L2 hit
  Penalty = 5ns/0.25ns = 20 cycles
L1 miss with L2 miss
  Extra penalty = 400 cycles
What is speedup of adding L2 cache?
CPI = 1 + 0.02 × 20 + 0.005 × 400 = 3.4 cycles/instruction
Speedup L2 = 9/3.4 = 2.6
CPU
L1 $
L2 $
Main Memory

## Slide 48: Multilevel Cache Considerations
L1 cache
  Focus on minimal hit time
  Usually separate L1 Instruction and L1 Data cache Why?
L2 cache
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact
  Shared I & D; why?
L3 cache
  Shared between all cores: why?
CPU
L1 $
L2 $
Main Memory
L3 $

## Slide 49: Splitting first level cache
Use split Instruction and Data caches
  Caches can be tuned differently
  Avoids dual ported cache
CPU
I$
D$
I&D
$
Main Memory
L1
L2

## Slide 50: Multi-level cache hierarchies; policies
Usually, cache inclusion is maintained
  When a block misses in L1 then it must be brought into all Li.
  When a block is replaced in Li, then it must be removed from all Lj, j<i
The opposite: exclusion
  If a block is in Li then it is not in any other cache level
  Miss in L1 then all copies are removed from all Li’s, i>1
  If a block is evicted from Li then this block is allocated in Li+1
Notes: Or no policy
We will assume inclusion; easier for coherency, but more costly (consumes more cache space)

## Slide 51: Classification of cache misses: 3 Cs
Compulsory (cold) misses: on the 1st reference to a block
Capacity misses: space is not sufficient to host data or code
Conflict misses: happen when two memory blocks map on the same cache block in direct-mapped or set-associative caches
Later we add Coherence misses ➔ 4 Cs classification
How to measure these misses?
  Cold misses: simulate infinite cache size
  Capacity misses: simulate fully associative cache then deduct cold misses
  Conflict misses: simulate cache then deduct cold and capacity misses

## Slide 52: 3Cs Absolute Miss Rate (on SPEC92)
Conflict
Miss rate per type

## Slide 53: 3Cs Relative Miss Rate (on SPEC92) same figure; now relative miss-rate i.s.o. absolute
Conflict
Miss rate per type
Notes: Same picture as previous slide, now plotted with 'relative' metric

## Slide 54: Part I
5 architecture alternatives (RISC is one of them)
What did you learn in Memory Hierarchy Part I ?
  Make yourself a recap !!
Some questions:
Write a program for a stack based architecture and show its operation
Why do we need a memory hierarchy?
Explain exactly how associative caches operate!
Translate cache metrics to instruction fields and vice-versa
Calculate the (multi-level) cache impact on CPI
How can we improve the cache & the memory hierarchy?
How to avoid collision misses? In HW? In SW?