## Slide 1: Embedded Computer Architecture 5SAI0 Multi-Threading & Multi-Processor Systems
Henk Corporaal
www.ics.ele.tue.nl/~heco/courses/ECA
h.corporaal@tue.nl
TUEindhoven
2021-2022

## Slide 2: Overview
Multi-threading architectures:
  Coarse grain multi-threading
  Fine-grain multi-threading
  SMT (simultaneous multi-threading)
    called hyperthreading by Intel
Multi-processing architectures
Material, our study books:
  Multi-threading
    H&P section 3.11: Multithreading
    Dubois e.a. section 8.3: SMT
  Multi-processing
    H&P: Chapter 5-5.2
    Dubois: Chapter 5-5.4.1

## Slide 3: New Approach: Multi-Threaded
Multithreading = multiple threads share the functional units of 1 processor
  duplicate independent state of each thread e.g., a separate copy of register file, a separate PC
  HW for fast thread switch; much faster than full process switch  100s to 1000s of clocks
When to switch?
  Fine grain: Next instruction is next thread, or
  Coarse grain: When a thread is stalled, perhaps for a cache miss, another thread can be executed

## Slide 4: Multithreaded Categories
Time (processor cycle)
Superscalar
Fine-Grained
Coarse-Grained
Multiprocessing
Simultaneous
Multithreading
Thread 1
Thread 2
Thread 3
Thread 4
Thread 5
Idle slot

## Slide 5: Fine-Grained Multithreading
Switches between threads on each instruction, causing the execution of multiples threads to be interleaved
Usually done in a round-robin fashion, skipping any stalled threads
CPU must be able to switch threads every clock
Advantage: it can hide both short and long stalls, since instructions from other threads executed when one thread stalls
Disadvantage: may slow down execution of individual threads
Used in e.g. Sun’s Niagara

## Slide 6: Course-Grained Multithreading
Switches threads only on costly stalls, such as L2 cache misses
Advantages
  Relieves need to have very fast thread-switching
  Doesn’t slow down thread, since instructions from other threads issued only when the thread encounters a costly stall
Disadvantage: hard to overcome throughput losses from shorter stalls, due to pipeline start-up costs
  Since CPU issues instructions from 1 thread, when a stall occurs, the pipeline must be emptied or frozen
  New thread must fill pipeline before instructions can complete
Because of this start-up overhead, coarse-grained multithreading is better for reducing penalty of high cost stalls, where pipeline refill << stall time
Used in e.g. IBM AS/400

## Slide 7: Simultaneous Multi-threading ...
1 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 
7 |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  | 
M
M
FX
FX
FP
FP
BR
CC
Cycle
One thread, 8 units
M = Load/Store, FX = Fixed Point, FP = Floating Point, BR = Branch, CC = Condition Codes
1 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 
7 |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  | 
M
M
FX
FX
FP
FP
BR
CC
Cycle
Two threads, 8 units

## Slide 8: Simultaneous Multithreading (SMT)
SMT: in each cycle operations from multiple threads can be issued and active
dynamically scheduled processors already has many HW mechanisms to support multithreading:
  Large set of virtual registers that can be used to hold the register sets of independent threads
  Register renaming provides unique register identifiers, so instructions from multiple threads can be mixed in datapath without confusing sources and destinations across threads
  Out-of-order completion allows the threads to execute out of order, and get better utilization of the HW
Just adding a per thread renaming table and keeping separate PCs

## Slide 9: IBM Power4
Single threaded
8 FUs
4-issue out-of-order

## Slide 10: IBM Power5
2 fetch (PC), 2 initial decodes
2 commits (architected register sets)
supports 2 threads

## Slide 11: Changes in Power 5 to support SMT
Increased associativity of L1 instruction cache and the instruction address translation buffers
Added per thread load and store queues
Increased size of the L2 (1.92 vs. 1.44 MB) and L3 caches
Added separate instruction prefetch and buffering per thread
Increased the number of virtual registers from 152 to 240
Increased the size of several issue queues
The Power5 core is about 24% larger than the Power4 core because of the addition of SMT support

## Slide 12: Power 5 thread performance ...
Relative priority of each thread controllable in hardware.
For balanced operation, both threads run slower than if they “owned” the machine.

## Slide 13: Multi-threading….
What is exactly Multi-Threading?
  how does it differ from multi-processing?
What processor changes are needed to support Multi-Threading?
What is the performance impact?
  running a single thread? When
  running multiple threads?
Do we need it?
  when?
Can you compare pros and cons of MT and Multi-Processing ?

## Slide 14: Overview
Multi-threading architectures
Multi-processing architectures
  Shared memory architectures
    symmetric
    distributed
  Message passing architectures
  Programming model
Material, our study books on multi-processing:
  H&P: Chapter 5-5.2
  Dubois: Chapter 5-5.4.1

## Slide 15: Should we go Multi-Processing?
Diminishing returns for exploiting ILP
  limited Instruction Level Parallelism costly to exploit
Power issues
Wiring issues (faster transistors do not help that much)
More vector and task-level parallel applications
Multi-core architectures hit all markets (even embedded)
  lower energy (due to same performance with lower Vdd)
  silicon technology still scales => abundance of transistors

## Slide 16
Trends:
since ~2003
  #transistors follows Moore
  but not freq. and performance/core
Core i7
3GHz
100W
5
Next?

## Slide 17: Example:Intel’s 72-core ‘Knight’s Landing’ XEON Phi
KNL 2016 introduced
14 nm
3D Tri-gate transistors
3 TFlops double / 6 TFlops single precision
512-bit SIMD/Vector processing per core
MCDRAM: multi-channel 3D stacked DRAM (like HBM, high BW mem.)

## Slide 18: Example: Intel’s 72-core ‘Knight’s Landing’ XEON Phi

## Slide 19: Multi-core Architecture
Parallel / Multi-core Architecture extends traditional computer architecture with a communication network
  abstractions (HW/SW interface)
  organizational structure to realize abstraction efficiently
Communication Network
Processing
node
Processing
node
Processing
node
Processing
node
Processing
node
Memory
I/O

## Slide 20: Parallel programming models
How parallel computations can be expressed in a high-level language?
  Simple extensions through an API (application-programming interface) of common programming languages such as C/C++ or FORTRAN:
    Shared-memory: OpenMP or Pthreads
    Message-passing: MPI (message-passing interface)
  Threads or processes must communicate and coordinate their activity (synchronization)
Who is parallizing your program?
  Parallelizing compilers translate a sequential program into parallel threads
  Yourself !

## Slide 21: Data vs function parallelism
Data parallelism:
  Partition the data set
    Apply the same function to each partition
  SPMD (= single program multiple data)
    SPMD ≠ SIMD; what's the difference?
  Massive parallelism
Function (Task-level) parallelism
  Partition the functionality
    Independent functions are executed on different processors
  E.g.: Streaming--software pipeline
  More complex, limited parallelism
Combine both: function + data parallelism

## Slide 22: Shared memory multiprocessors
Key characteristics:
  all memory addresses visible by every processor
  inter-processor communication by (normal) loads and stores
  synchronization needed to control order between loads and store (for proper communication)
Communication Network
Processing
node
Processing
node
Processing
node
Processing
node
Processing
node
Memory
I/O
Memory

## Slide 23: Communication models: Shared Memory
Process P1
Process P2
Shared
Memory
3 Problems:
  Coherence problem
  Memory consistency issue
  Synchronization problem
(read, write)
(read, write)

## Slide 24: Shared memory multiprocessors: Type 1
Symmetric multiprocessors (SMP)
Small number of cores
Share single memory with uniform memory latency

## Slide 25: Shared memory multiprocessors: Type 2
Distributed shared memory (DSM)
  Memory distributed among processors
  Non-uniform memory access/latency (NUMA)
  Processors connected via direct (switched) and non-direct (multi-hop) interconnection networks

## Slide 26: Four Cache organizations for SMPs
Rest of discussion considers organizations (c) and (d)

## Slide 27: Example: matrix multiply + sum
Sequential program:
1 sum = 0;
2 for (i=0,i<n, i++)
3 for (j=0,j<n, j++){
4 C[i,j] = 0;
5 for (k=0,k<n, k++)
6 C[i,j] = C[i,j] + A[i,k]*B[k,j];
7 sum += C[i,j];
8 }
- Multiply A[n,n] by B[n,n] and store result in C[n,n]
- Add all elements of matrix C

## Slide 28: Shared mem: matrix multiply + sum
Mutual exclusion
/* A, B, C, bar, lv and sum are shared, all others are private
*/
1a low = pid*n/nproc; /pid=0...Nproc-1; pid= processor ID
1b hi = low + n/nproc; /each proc sums n/nproc rows
1c mysum = 0; sum = 0; /low to hi
2 for (i=low,i<hi, i++)
3 for (j=0,j<n, j++){
4 C[i,j] = 0;
5 for (k=0,k<n, k++)
6 C[i,j] = C[i,j] + A[i,k]*B[k,j];
7 mysum +=C[i,j]; /C summed in shared memory
8 }
9 barrier(bar);
10 lock(lv);
sum += mysum;
unlock(lv);
Synchronization

## Slide 29: Why Mutual Exclusion?
Assume the following statements are executed by 2 threads, T1 and T2, on sum
T1 T2
sum<- sum+1 sum<- sum+1
Compiled code on a RISC machine includes several instructions
A possible interleaving of execution is:
T1 T2
r1 <- sum
R1 <- sum
r1 <- r1 + 1
r1 <- r1 + 1
sum <- r1
sum <- r1
At the end the result is that sum is incremented by 1 (not 2)
time

## Slide 30: Communication models: Message Passing
Communication primitives
  e.g., send, receive library calls
  standard MPI: Message Passing Interface
    www.mpi-forum.org
Note that MP can be build on top of SM and vice versa !
Process P1
Process P2
receive
receive
send
send
FiFO

## Slide 31: Message Passing Model
Explicit message send and receive operations:
  Send specifies local buffer + receiving process on remote computer
  Receive specifies sending process on remote computer + local buffer to place data
Typically blocking communication, but may use DMA
  DMA = Direct Memory Access (check this out!)
Header
Data
Trailer
Message structure

## Slide 32: Message passing communication
Interconnection Network
Network
interface
Network
interface
Network
interface
Network
interface
Cache
Processor
Memory
DMA
Cache
Processor
Memory
DMA
Cache
Processor
Memory
DMA
Cache
Processor
Memory
DMA

## Slide 33: Synchronous message-passing
Thread T1: Thread T2:
a = 10; b = 5;
send(&a,sizeof(a),t2,send_a); recv(&b,sizeof(b),t1,send_a);
a = a+1; b=b+1;
recv(&a,sizeof(a),t2,send_b); send(&b,sizeof(b),t1,send_b);
printf(a);
Each send/recv has 4 operands:
  Starting address in memory
  Size of message
  Destination/source thread id
  Tag connecting sends and receives
Synchronous communication =
  sender blocks until recv is completed and receiver blocks until message has been sent
What value is printed under synchronous MP?
Tag, not always
needed; why not?

## Slide 34: Message-passing: matrix multiply + sum
Notes:
pid = process id
pid 0 is the controlling process, distributing data, collecting results
compare shared memory solution (slide 28); what are differences?

## Slide 35: Synchronous message-passing
Advantage:
  Communication protocol enforces synchronization
Disadvantages:
  Prone to deadlock
  Block threads: no overlap of communication with computation
Deadlock example:
thread T1: thread T2:
a = 10; b = 5;
send(&a,sizeof(a),t2,send_a); send(&b,sizeof(b),t1,send_b)
recv(&c,sizeof(c),t2,send_b); recv(&d,sizeof(d),t1,send_a);
To eliminate the deadlock: swap the send/recv pair in T2,
or employ asynchronous message-passing

## Slide 36: (A)Synchronous message-passing
thread T1: thread T2:
a = 10; b = 5;
asend(&a,sizeof(a),t2,send_a); asend(&b,sizeof(b),t1,send_b);
<unrelated computation;> <unrelated computation;>
srecv(&b,sizeof(b),t2,send_b); srecv(&a,sizeof(b),t1,send_a);

## Slide 37: (A)Synchronous message-passing
In general multiple threads are running on a core
This handshake is for synchronous message passing
Can also be applied to blocking or non-blocking asynchronous
  Sender continues after send (a) and receiver after recv (b)
    If blocking, sender must make a copy of message first

## Slide 38: Support for message passing protocols
Data must be copied from/to memory to/from NI (= Network Interface)
  Processor could do it
  DMA (direct memory access) unit can speed up message transfers and off-load the processor
    programmed by the processor by specifying start address and size
Dedicated message processors
  Use a special processor to process messages on both ends
  Thus relieving the compute O/S from doing it
Support for user-level messages by OS (operating system):
  DMA engine controlled by OS
  Message is copied from user space to system space (send)
  Message is first copied into system space and then into user space (receive)
  Tag user messages so that they are picked up and delivered directly in user memory space (zero copy)

## Slide 39: Message-passing support

## Slide 40: Communication Models: Shared-Memory vs Message Passing
Shared-Memory (used by e.g. OpenMP)
  Compatibility with well-understood (language) mechanisms
  Ease of programming for complex or dynamic communications patterns
  Shared-memory applications; sharing of large data structures
  Efficient for small items
  Supports hardware caching
Messaging Passing (used by e.g. MPI)
  Simpler hardware
  Explicit communication
  Implicit synchronization (with any communication)
What do you prefer?

## Slide 41: Next: 3 fundamental issues for shared memory multiprocessors
Coherence, about: Do I see the most recent data?
Consistency, about: When do I see a written value?
  e.g. do different processors see writes at the same time (w.r.t. other memory accesses)?
Synchronization How to synchronize processes?
  how to protect access to shared data?

## Slide 42: Concluding remarks
Number of transistors still scales well (how long?)
However power/energy limits reached
Frequency not further increased
Therefore: After 2003 going Multi-Core
  exploiting task / thread level parallelism (TLP)
  can be combined with exploiting DLP (SIMD / Sub-word parallelism)
2 types of systems and programming models
  Shared memory
  Message passing
  What are the pros and cons of both systems?