## Slide 1: Computer Vision for Autonomous Systems
Read Szeliski 4.1
Credit for slides by Kristen Grauman, Robert Collins, Derek Hoiem, Alyosha Efros, and Svetlana Lazebnik
dr. Egor Bondarev
VCA/SPS group
TUE

## Slide 2: My Research Interests: 3D sensing
Set of 2D/3D Sensing Platforms
Few laser-scanner platforms (LIDARs)
RGB-D mapping system (Kinect)
Stereo Cameras, Panoramic 360 camera
Autonomous robot
PAGE 1

## Slide 3: 2D/3D Data Fusion Pipeline
Point
-
clouds from laser-scan
Image samples from 360-camera
Generated 3D meshed model
3D model with mapped texture
Total volumetric 3D model
Point
-
cloud filtering &
Mesh generation
Mapping the textures
on meshes
Enhancement &
Alignment of meshes
Notes: In recent years, there is a growing availability of various 3D modeling systems, such as LIDAR platforms and extended RGB-D mapping systems.

## Slide 4: Detailed Reconstruction & Texturing
Notes: The generation of 3D models of the real world environment is of high interest to many fields, including professional civil engineering, environment-based game design, robotics and ect.

## Slide 5: Results: Complex-shape Spaces
Notes: The generation of 3D models of the real world environment is of high interest to many fields, including professional civil engineering, environment-based game design, robotics and ect.

## Slide 6: Results: Extremely Large Spaces
Notes: The generation of 3D models of the real world environment is of high interest to many fields, including professional civil engineering, environment-based game design, robotics and ect.

## Slide 7: Demos: 3D room reconstruction

## Slide 8: Computer Vision
Make computers understand images and videos
What kind of scene?
Where the camera is located at this scene?
Where are the cars?
How far is the building?

## Slide 9: Components of a computer vision system
Lighting
Scene
Camera
Computer
Scene Interpretation

## Slide 10: Application Domains
wiki
HCI

## Slide 11: Application for Robotics
wiki
HCI

## Slide 12: Vision in Robotics
Major Goals
  Identify camera (robot) position and orientation at every moment in time - localization
  Understand the obstacles - mapping
  Compute best path

## Slide 13: Vision in Robotics
Major Goals
  Identify camera (robot) position and orientation at every moment in time - localization
  Understand the obstacles - mapping
  Compute best path
  Analyse images obtained at X Hz frequency
    Compute the camera pose from feature points on the images
  Computation speed is important
    30 Hz frequency  33 ms deadline
  Alternative (complementary) ways exist
    GPS, Accelerometer, Gyroscope, Barometer, Laser, Compass, etc

## Slide 14: Common Pipeline for Localization
Identify features on image
Describe & store the features
Find correlated features on next image
Compute image-level transformation
Images from Copter
Copter position and orientation
From images to drone position & orientation
Feature detection
Feature description
Matching
Transformation matrix

## Slide 15: The whole pipeline in crash: Localize robot using feature points

## Slide 16: Motion illusion, rotating snakes

## Slide 17: Interest points
“interest points” = “keypoints”, also sometimes called “features”
Feature detection
Feature description
Matching
Transformation matrix
Keypoints should be repeatable and distinctive
B1
B2
B3
A1
A2
A3

## Slide 18: Goals for Keypoints
Detect points that are repeatable and distinctive
Feature detection
Feature description
Matching
Transformation matrix

## Slide 19: Key trade-offs
More Repeatable
More Points
B1
B2
B3
A1
A2
A3
Detection of interest points
More Distinctive
More Flexible
Description of patches
Robust to occlusion
Works with less texture
Minimize wrong matches
Robust to expected variations
Maximize correct matches
Robust detection
Precise localization
Feature detection
Feature description
Matching
Transformation matrix

## Slide 20: Overview of Keypoint Matching
B1
B2
B3
A1
A2
A3
1. Find a set of distinctive key- points
3. Extract and normalize the region content
2. Define a region around each keypoint
4. Compute a local descriptor from the normalized region
5. Match local descriptors
Feature detection
Feature description
Matching
Transformation matrix

## Slide 21: Invariant Local Features
Image content is transformed into local feature coordinates that are invariant to translation, rotation, scale, and other imaging parameters
Features Descriptors
Feature detection
Feature description
Matching
Transformation matrix

## Slide 22: Characteristics of good features
Repeatability
  The same feature can be found in several images despite geometric and photometric transformations
Saliency
  Each feature is distinctive
Compactness and efficiency
  Many fewer features than image pixels
Locality
  A feature occupies a relatively small area of the image; robust to clutter and occlusion
Feature detection
Feature description
Matching
Transformation matrix

## Slide 23: Many Existing Features Available
Hessian & Harris [Beaudet ‘78], [Harris ‘88]
Laplacian, DoG [Lindeberg ‘98], [Lowe 1999]
Harris-/Hessian-Laplace [Mikolajczyk & Schmid ‘01]
Harris-/Hessian-Affine [Mikolajczyk & Schmid ‘04]
EBR and IBR [Tuytelaars & Van Gool ‘04]
MSER [Matas ‘02]
Salient Regions [Kadir & Brady ‘01]
Others…
Feature detection
Feature description
Matching
Transformation matrix

## Slide 24: Corner Detection: Basic Idea
We should easily recognize the point by looking through a small window
Shifting a window in any direction should give a large change in intensity
“edge”: no change along the edge direction
“corner”: significant change in all directions
“flat” region: no change in all directions
Source: A. Efros
Feature detection
Feature description
Matching
Transformation matrix

## Slide 25: Finding Corners
Key property: in the region around a corner, image gradient has two or more dominant directions
Corners are repeatable and distinctive
C.Harris and M.Stephens. "A Combined Corner and Edge Detector.“ Proceedings of the 4th Alvey Vision Conference: pages 147--151.
Feature detection
Feature description
Matching
Transformation matrix

## Slide 26: Robustness problem: covariance
We want corner locations to be covariant to geometric transformations
  Covariance: if we have two transformed versions of the same image, features should be detected in corresponding locations
Feature detection
Feature description
Matching
Transformation matrix

## Slide 27: Image translation - for corner feature
Derivatives and window function are shift-invariant
Corner location is covariant w.r.t. translation
Feature detection
Feature description
Matching
Transformation matrix

## Slide 28: Image rotation for corner feature
Second moment ellipse rotates but its shape (i.e. eigenvalues) remains the same
Corner location is covariant w.r.t. rotation
Feature detection
Feature description
Matching
Transformation matrix

## Slide 29: Scaling of corner feature
All points will be classified as edges
Corner
Corner location is not covariant to scaling!
Need for improvement: multi-scale patches around the feature
Feature detection
Feature description
Matching
Transformation matrix

## Slide 30: So far: can localize in x-y, but not scale
Feature detection
Feature description
Matching
Transformation matrix

## Slide 31: Automatic Scale Selection
Function responses for increasing scale (scale signature)
Feature detection
Feature description
Matching
Transformation matrix

## Slide 32: Automatic Scale Selection
Function responses for increasing scale (scale signature)
Feature detection
Feature description
Matching
Transformation matrix

## Slide 33: Automatic Scale Selection
Function responses for increasing scale (scale signature)
Feature detection
Feature description
Matching
Transformation matrix

## Slide 34: Automatic Scale Selection
Function responses for increasing scale (scale signature)
Feature detection
Feature description
Matching
Transformation matrix

## Slide 35: Automatic Scale Selection
Function responses for increasing scale (scale signature)
Feature detection
Feature description
Matching
Transformation matrix

## Slide 36: Automatic Scale Selection
Function responses for increasing scale (scale signature)
Feature detection
Feature description
Matching
Transformation matrix

## Slide 37: Automatic Scale Selection
How to find corresponding patch sizes (scale)?
Feature detection
Feature description
Matching
Transformation matrix

## Slide 38: Multi-scale Patching Sampling & Filtering
Feature detection
Feature description
Matching
Transformation matrix
Background on Sampling and Filtering

## Slide 39
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering: box filter
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Feature detection
Feature description
Matching
Transformation matrix
Notes: ones, divide by 9

## Slide 40
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 | 30 | 30 | 20 | 10 | 
 | 0 | 20 | 40 | 60 | 60 | 60 | 40 | 20 | 
 | 0 | 30 | 60 | 90 | 90 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 20 | 30 | 50 | 50 | 60 | 40 | 20 | 
 | 10 | 20 | 30 | 30 | 30 | 30 | 20 | 10 | 
 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 
Image filtering: box filter
Credit: S. Seitz
1
1
1
1
1
1
1
1
1
Feature detection
Feature description
Matching
Transformation matrix

## Slide 41
Weight contributions of neighboring pixels by nearness
0.003 0.013 0.022 0.013 0.003
0.013 0.059 0.097 0.059 0.013
0.022 0.097 0.159 0.097 0.022
0.013 0.059 0.097 0.059 0.013
0.003 0.013 0.022 0.013 0.003
5 x 5,  = 1
Slide credit: Christopher Rasmussen
Important filter: Gaussian
Feature detection
Feature description
Matching
Transformation matrix
Notes: e^0 = 1, e^-1 = .37, e^-2 = .14, etc.

## Slide 42
Throw away every other row and column to create a 1/2 size image
Subsampling by a factor of 2
Feature detection
Feature description
Matching
Transformation matrix

## Slide 43: Subsampling with Gaussian pre-filtering
G 1/4
G 1/8
Gaussian 1/2
Slide by Steve Seitz
Feature detection
Feature description
Matching
Transformation matrix

## Slide 44: DoG – Efficient Computation
Computation in Gaussian scale pyramid
s
Original image
Sampling with step s4 =2
s
s
s
Feature detection
Feature description
Matching
Transformation matrix

## Slide 45: Find local maxima in position-scale space of Difference-of-Gaussian
s
s2
s3
s4
s5
 List of (x, y, s)
Feature detection
Feature description
Matching
Transformation matrix
Notes: Blob detector is distinct from harris corner detector

## Slide 46: Results: Difference-of-Gaussian
Feature detection
Feature description
Matching
Transformation matrix

## Slide 47: Automatic Scale Selection
Corresponding patch sizes found using subsampling and filtering.
Feature detection
Feature description
Matching
Transformation matrix

## Slide 48: Feature Description: SIFT
Feature Description:
  SIFT - Scale Invariant Feature Transform
  SURF – Efficient approximation of SIFT
Feature detection
Feature description
Matching
Transformation matrix

## Slide 49: SIFT Phases
Constructing a scale space
Laplacian of Gaussian approximation (DoG)
Finding keypoints
Eliminate edges and low contrast regions
Assigning Keypoint Orientation
Generate SIFT features
Feature detection
Feature description
Matching
Transformation matrix

## Slide 50: SIFT Phases
Constructing a scale space
Laplacian of Gaussian approximation (DoG)
Finding keypoints
Eliminate edges and low contrast regions
Assigning Keypoint Orientation
Generate SIFT features
Concepts reused from discussed Multi-scale Corner Detection
Feature detection
Feature description
Matching
Transformation matrix

## Slide 51: SIFT: Assigning Keypoint Orientation
Take found keypoint
Compute gradients for pixels around
Assign dominant orientation as a keypoint orientation
Compute
histogram of gradients
Feature detection
Feature description
Matching
Transformation matrix

## Slide 52: SIFT
By now, our keypoint description is invariant to:
  Translation
  Rotation
  Scale
Lets make it descriptive for further matching!
Feature detection
Feature description
Matching
Transformation matrix

## Slide 53: SIFT: Description Generation
4x4 array of gradient orientation histogram weighted by magnitude
8 orientations x 4x4 array = 128 dimensions
showing only 2x2 here but is 4x4
Feature detection
Feature description
Matching
Transformation matrix

## Slide 54: SIFT: Repeatability
Best repeatability among all other feature descriptors
Besides this
  Robust and Distinctive
  Compact and Efficient
Feature detection
Feature description
Matching
Transformation matrix

## Slide 55: SURF descriptor
Fast approximation of SIFT idea
  Efficient computation by 2D box filters & integral images  6 times faster than SIFT
  Equivalent quality for object identification
[Bay, ECCV’06], [Cornelis, CVGPU’08]
GPU implementation available
  Feature extraction @ 200Hz (detector + descriptor, 640×480 img)
  http://www.vision.ee.ethz.ch/~surf
Feature detection
Feature description
Matching
Transformation matrix

## Slide 56: Feature Matching
Feature detection
Feature description
Matching
Transformation matrix

## Slide 57: Feature Matching
Simple criteria: One feature matches to another if those features are nearest neighbors and their distance is below some threshold.
Problems:
  Threshold is difficult to set
  Non-distinctive features could have lots of close matches, only one of which is correct
Feature detection
Feature description
Matching
Transformation matrix

## Slide 58: SIFT (Vector Feature) Matching
Take one of the keypoint descriptor from one image.
Find the Euclidean distance between the keypoint descriptor u taken and the keypoint descriptors of other image.
  Now, you have the Euclidean distances of one keypoint in image1 to all the keypoints in image2.
  Arrange them in ascending order.(It implies the nearest distances for keypoint in image1 to keypoints in image2)
Set some threshold T ( mostly in the range 0.3 to 0.7).
Take the ratio of first nearest distance to second nearest distance and would be less than this threshold, then only it is a match and save that index. otherwise there is no match.
Repeat this for all keypoint descriptos in image1.
Euclidean Distance computation
Feature detection
Feature description
Matching
Transformation matrix

## Slide 59: Binary Feature Matching
Standalone, works only for small changes in camera view
When camera view changes are large 
  should be coupled with next step: Estimation of Transformation Matrix
Feature detection
Feature description
Matching
Transformation matrix

## Slide 60: Binary Feature Matching
How to find landmarks to match across two images?
How to distinguish one landmark from another?
How to match N landmarks from I1 to M landmarks from I2, assuming that I2 has more and less than I1 ?
Feature detection
Feature description
Matching
Transformation matrix

## Slide 61: General matching notions
Pj are points (or “parts”) in first image
Lk are labels in second image or model; these could be points, parts, or interpretations of them
Need to match some pairs (Pj , Lk): can be combinatorially expensive
P1
L1
P2
P3
Pj
L2
L3
Lk
L4
There are many mappings from Image 1 pts to Image 2 labels.
Feature detection
Feature description
Matching
Transformation matrix

## Slide 62: Constraining the mapping
Points may have distinguishing features
Points may be distinguished by relations with neighbor points or regions
Points may be distinguished by distance relations with distant points
Points or corners might be connected to others
Feature detection
Feature description
Matching
Transformation matrix

## Slide 63: Constraining the mapping
CVPR04 Stockman (27 June 04)
By unique intensity/color structure of neighborhood
By geometry or topology of neighborhood
Image 1
Image 2
Vectors show how intensity neighborhoods moved: similar vectors are colored the same
Feature detection
Feature description
Matching
Transformation matrix

## Slide 64: Can match minimal spanning trees
Extract minimal spanning trees from points of I1 and of I2
Assumption is that spanning tree structure is robust to some errors in point extraction
Select tree nodes with high degree
Below example: match 3 nodes of same degree and verify a consistent RS&T mapping
P1
L1
L2
P2
P3
L3
Feature detection
Feature description
Matching
Transformation matrix

## Slide 65: Binary feature matching
Large view changes – combine with transformation matrix computation
Feature detection
Feature description
Matching
Transformation matrix

## Slide 66: At last Computing Transformation Matrix: Rotation and Translation of Camera Localization of the drone
Feature detection
Feature description
Matching
Transformation matrix

## Slide 67: Structure from motion
Given a set of corresponding points in two or more images, compute the camera parameters and the 3D point coordinates
Camera 1
Camera 2
Camera 3
R1,t1
R2,t2
R3,t3
?
?
?
?
Feature detection
Feature description
Matching
Transformation matrix
Notes: Structure from motion solves the following problem:
Given a set of images of a static scene with 2D points in correspondence, shown here as color-coded points, find…
a set of 3D points P and
a rotation R and position t of the cameras that explain the observed correspondences. In other words, when we project a point into any of the cameras, the reprojection error between the projected and observed 2D points is low.
This problem can be formulated as an optimization problem where we want to find the rotations R, positions t, and 3D point locations P that minimize sum of squared reprojection errors f. This is a non-linear least squares problem and can be solved with algorithms such as Levenberg-Marquart. However, because the problem is non-linear, it can be susceptible to local minima. Therefore, it’s important to initialize the parameters of the system carefully. In addition, we need to be able to deal with erroneous correspondences.

## Slide 68
Projection matrix
x: Image Coordinates: (u,v,1)
K: Intrinsic Matrix (3x3)
R: Rotation (3x3)
t: Translation (3x1)
X: World Coordinates: (X,Y,Z,1)
Ow
iw
kw
jw
R,T
Feature detection
Feature description
Matching
Transformation matrix
Notes: We can use homogeneous coordinates to write camera matrix in linear form.

## Slide 69
K
Projection matrix
Intrinsic Assumptions
Unit aspect ratio
Optical center at (0,0)
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
Feature detection
Feature description
Matching
Transformation matrix
Notes: Work through equations for u and v on board

## Slide 70: Allow camera translation
Intrinsic Assumptions
Extrinsic Assumptions
No rotation
Feature detection
Feature description
Matching
Transformation matrix

## Slide 71: 3D Rotation of Points
Rotation around the coordinate axes, counter-clockwise:
p
p’
g
y
z
Slide Credit: Saverese
Feature detection
Feature description
Matching
Transformation matrix

## Slide 72: Allow camera rotation
Feature detection
Feature description
Matching
Transformation matrix

## Slide 73
Geometry of two views constrains where the corresponding pixel for some image point in the first view must occur in the second view.
  It must be on the line carved out by a plane connecting the world point and optical centers.
Epipolar constraint
Feature detection
Feature description
Matching
Transformation matrix
Notes: 72

## Slide 74
Epipolar Plane
Epipole
Epipolar Line
Baseline
Epipolar geometry
Epipole
http://www.ai.sri.com/~luong/research/Meta3DViewer/EpipolarGeo.html
Feature detection
Feature description
Matching
Transformation matrix
Notes: 73

## Slide 75
Baseline: line joining the camera centers
Epipole: point of intersection of baseline with image plane
Epipolar plane: plane containing baseline and world point
Epipolar line: intersection of epipolar plane with the image plane
Epipolar geometry: terms
Why is the epipolar constraint useful?
Feature detection
Feature description
Matching
Transformation matrix
Epipolar Plane
Epipole
Epipolar Line
Baseline
Epipole

## Slide 76
Epipolar constraint
This is useful because it reduces the feature correspondence search problem to a 1D search along an epipolar line.
Image from Andrew Zisserman
Feature detection
Feature description
Matching
Transformation matrix

## Slide 77
Example: converging cameras
Figure from Hartley & Zisserman
Feature detection
Feature description
Matching
Transformation matrix
Notes: 76

## Slide 78: Example: Forward motion
What would the epipolar lines look like if the camera moves directly forward?
Feature detection
Feature description
Matching
Transformation matrix

## Slide 79: Example: Forward motion
e
e’
Epipole has same coordinates in both images.
Points move along lines radiating from e: “Focus of expansion”
Feature detection
Feature description
Matching
Transformation matrix

## Slide 80: Fundamental matrix
Let p be a point in left image, p’ in right image
Epipolar relation
  p maps to epipolar line l’
  p’ maps to epipolar line l
Epipolar mapping described by a 3x3 matrix F
l’
l
p
p’
Feature detection
Feature description
Matching
Transformation matrix

## Slide 81: Fundamental matrix
This matrix F is called
  the “Essential Matrix”
    E: when image intrinsic parameters are known
  the “Fundamental Matrix”
    F: more generally (uncalibrated case)
  the “Homography Matrix”
    H: Degenerate case of Fundamental matrix
    In case if baseline is small (rotating around)
    Or camera views are on the plane (not 3D space)
Feature detection
Feature description
Matching
Transformation matrix

## Slide 82: Fundamental matrix
Can solve for F from point correspondences
  Each (p, p’) pair gives one linear equation in entries of F
  F has 9 entries [3x3], but really only 7 or 8 degrees of freedom.
  With 8 points it is simple to solve for F.
  Possible with 7 points also.
Feature detection
Feature description
Matching
Transformation matrix

## Slide 83: Computing F: 8-point algorithm
Solve a system of homogeneous linear equations
  Write down the system of equations
Feature detection
Feature description
Matching
Transformation matrix

## Slide 84: Last Step: From F/E to Translation & Rotation of Camera
Use Singular Value Decomposition (SVD) method.
  E is the Essential Matrix (FE, in case camera intrinsics known )
  ,where U V and are orthogonal matrices, and
  Then
  Camera Rotation:
  Camera Translation:
  , where
Validate SVD result:
Feature detection
Feature description
Matching
Transformation matrix

## Slide 85: Challenges
SVD yields many Rt solutions
 find high confidence solution via factorization
Taken N points never provide ideal local & global correspondence (noise, matching errors, outliers, occlusions)
 use RANSAC for highest confidence Rt solution
 run Bundle Adjustment:
    Non-linear method for refining structure and motion
    Minimizing reprojection error
 refine the found Rt solution with Global Iterative Closest Point method
Feature detection
Feature description
Matching
Transformation matrix

## Slide 86: Challenges
Frame-to-frame drift (incorrect Rt to ground-truth)
Global drift increases over time
  Solve with Loop Closure technique
  Complement visual tracking with other sensors: IMU, GPS, compass, barometer, depth, etc.
Feature detection
Feature description
Matching
Transformation matrix

## Slide 87: Structure from Motion
Given a set of corresponding points in two or more images, compute the camera parameters and the 3D point coordinates
Camera 1
Camera 2
Camera 3
R1,t1
R2,t2
R3,t3
Feature detection
Feature description
Matching
Transformation matrix
Notes: Structure from motion solves the following problem:
Given a set of images of a static scene with 2D points in correspondence, shown here as color-coded points, find…
a set of 3D points P and
a rotation R and position t of the cameras that explain the observed correspondences. In other words, when we project a point into any of the cameras, the reprojection error between the projected and observed 2D points is low.
This problem can be formulated as an optimization problem where we want to find the rotations R, positions t, and 3D point locations P that minimize sum of squared reprojection errors f. This is a non-linear least squares problem and can be solved with algorithms such as Levenberg-Marquart. However, because the problem is non-linear, it can be susceptible to local minima. Therefore, it’s important to initialize the parameters of the system carefully. In addition, we need to be able to deal with erroneous correspondences.

## Slide 88: Recap
Identify features on image
Describe & store the features
Find correlated features on next image
Compute image-level transformation
Images from Copter
Copter position and orientation
From images to drone position & orientation

## Slide 89: Recap
Identify features on image
Describe & store the features
Find correlated features on next image
Compute image-level transformation
Images from Copter
Copter position and orientation
From images to drone position & orientation
Computationally expensive
For low-cost platform
& slow motion:
  Optical flow
  Kalman filter

## Slide 90: Useful info & links
Open Source SW:
  OpenCV library – vision algorithms, opencv.org
  PCL library – depth-based vision algorithms, pointclouds.org
Middleware / Firmware / Drivers
  ROS library – control and vision, other sensors, www.ros.org
  PIXHAWK middleware
    Computer Vision Flight – Autonomous navigation using computer vision, https://pixhawk.ethz.ch/software/computer_vision/flight
  APM Copter
    http://copter.ardupilot.com/
All in one kits:
  ArduCopter, http://store.3drobotics.com/products/3dr-arducopter-quad-c-frame-kit-1
  IRIS, http://store.3drobotics.com/products/iris

## Slide 91: Annex
Corner Point Detection
Mathematics required for
Optical Flow tracking

## Slide 92: Finding Corners
Key property: in the region around a corner, image gradient has two or more dominant directions
Corners are repeatable and distinctive
C.Harris and M.Stephens. "A Combined Corner and Edge Detector.“ Proceedings of the 4th Alvey Vision Conference: pages 147--151.

## Slide 93: Corner Detection: Mathematics
Change in appearance of window w(x,y)
for the shift [u,v]:
I(x, y)
E(u, v)
E(3,2)
w(x, y)

## Slide 94: Corner Detection: Mathematics
I(x, y)
E(u, v)
E(0,0)
w(x, y)
Change in appearance of window w(x,y)
for the shift [u,v]:

## Slide 95: Corner Detection: Mathematics
Intensity
Shifted intensity
Window function
or
Window function w(x,y) =
Gaussian
1 in window, 0 outside
Source: R. Szeliski
Change in appearance of window w(x,y)
for the shift [u,v]:

## Slide 96: Corner Detection: Mathematics
We want to find out how this function behaves for small shifts
Change in appearance of window w(x,y)
for the shift [u,v]:
E(u, v)

## Slide 97: Corner Detection: Mathematics
Local quadratic approximation of E(u,v) in the neighborhood of (0,0) is given by the second-order Taylor expansion:
We want to find out how this function behaves for small shifts
Change in appearance of window w(x,y)
for the shift [u,v]:

## Slide 98: Corner Detection: Mathematics
Second-order Taylor expansion of E(u,v) about (0,0):

## Slide 99: Corner Detection: Mathematics
Second-order Taylor expansion of E(u,v) about (0,0):

## Slide 100: Corner Detection: Mathematics
Second-order Taylor expansion of E(u,v) about (0,0):

## Slide 101: Corner Detection: Mathematics
The quadratic approximation simplifies to
where M is a second moment matrix computed from image derivatives:
M

## Slide 102
Corners as distinctive interest points
2 x 2 matrix of image derivatives (averaged in neighborhood of a point).
Notation:

## Slide 103: Interpreting the second moment matrix
The surface E(u,v) is locally approximated by a quadratic form. Let’s try to understand its shape.

## Slide 104: Interpreting the second moment matrix
First, consider the axis-aligned case (gradients are either horizontal or vertical)
If either λ is close to 0, then this is not a corner, so look for locations where both are large.

## Slide 105: Interpreting the second moment matrix
Consider a horizontal “slice” of E(u, v):
This is the equation of an ellipse.

## Slide 106: Interpreting the second moment matrix
Consider a horizontal “slice” of E(u, v):
This is the equation of an ellipse.
The axis lengths of the ellipse are determined by the eigenvalues and the orientation is determined by R
direction of the slowest change
direction of the fastest change
(max)-1/2
(min)-1/2
Diagonalization of M:

## Slide 107: Visualization of second moment matrices

## Slide 108: Visualization of second moment matrices

## Slide 109: Interpreting the eigenvalues
1
2
“Corner” 1 and 2 are large, 1 ~ 2; E increases in all directions
1 and 2 are small; E is almost constant in all directions
“Edge” 1 >> 2
“Edge” 2 >> 1
“Flat” region
Classification of image points using eigenvalues of M:

## Slide 110: Corner response function
“Corner” R > 0
“Edge” R < 0
“Edge” R < 0
“Flat” region
|R| small
α: constant (0.04 to 0.06)

## Slide 111: Harris corner detector
Compute M matrix for each image window to get their cornerness scores.
Find points whose surrounding window gave large corner response (f> threshold)
Take the points of local maxima, i.e., perform non-maximum suppression
C.Harris and M.Stephens. “A Combined Corner and Edge Detector.” Proceedings of the 4th Alvey Vision Conference: pages 147—151, 1988.
Notes: 110

## Slide 112: Harris Detector [Harris88]
Second moment matrix
1. Image derivatives
2. Square of derivatives
3. Gaussian filter g(sI)
Ix
Iy
Ix2
Iy2
IxIy
g(Ix2)
g(Iy2)
g(IxIy)
4. Cornerness function – both eigenvalues are strong
har
5. Non-maxima suppression
(optionally, blur first)

## Slide 113: Annex
Tracking based on Optical Flow

## Slide 114: This class: recovering motion
Feature-tracking
  Extract visual features (corners, textured areas) and “track” them over multiple frames
Optical flow
  Recover image motion at each pixel from spatio-temporal image brightness variations (optical flow)
B. Lucas and T. Kanade. An iterative image registration technique with an application to
stereo vision. In Proceedings of the International Joint Conference on Artificial Intelligence, pp. 674–679, 1981.
Two problems, one registration method

## Slide 115: Feature tracking
Many problems, such as structure from motion require matching points
If motion is small, tracking is an easy way to get them

## Slide 116: Feature tracking
Challenges
  Figure out which features can be tracked
  Efficiently track across frames
  Some points may change appearance over time (e.g., due to rotation, moving into shadows, etc.)
  Drift: small errors can accumulate as appearance model is updated
  Points may appear or disappear: need to be able to add/delete tracked points

## Slide 117: Feature tracking
Given two subsequent frames, estimate the point translation
Key assumptions of Lucas-Kanade Tracker
  Brightness constancy: projection of the same point looks the same in every frame
  Small motion: points do not move very far
  Spatial coherence: points move like their neighbors
I(x,y,t)
I(x,y,t+1)

## Slide 118: The brightness constancy constraint
Brightness Constancy Equation:
Take Taylor expansion of I(x+u, y+v, t+1) at (x,y,t) to linearize the right side:
I(x,y,t)
I(x,y,t+1)
Hence,
Image derivative along x
Difference over frames
Notes: Brightness constancy equation is equivalent to minimizing the squared error of I(t) and I(t+1)
http://en.wikipedia.org/wiki/Taylor_series
In mathematics, a Taylor series is a representation of a function as an infinite sum of terms that are calculated from the values of the function's derivatives at a single point. http://en.wikipedia.org/wiki/Taylor_series#Taylor_series_in_several_variables

## Slide 119: How does this make sense?
What do the static image gradients have to do with motion estimation?

## Slide 120: The brightness constancy constraint
How many equations and unknowns per pixel?
The component of the motion perpendicular to the gradient (i.e., parallel to the edge) cannot be measured
edge
(u,v)
(u’,v’)
gradient
(u+u’,v+v’)
  If (u, v) satisfies the equation, so does (u+u’, v+v’ ) if
  One equation (this is a scalar equation!), two unknowns (u,v)
Can we use this equation to recover image motion (u,v) at each pixel?
Notes: A: u and v are unknown, 1 equation

## Slide 121: Solving the ambiguity…
How to get more equations for a pixel?
Spatial coherence constraint
Assume the pixel’s neighbors have the same (u,v)
  If we use a 5x5 window, that gives us 25 equations per pixel
B. Lucas and T. Kanade. An iterative image registration technique with an application to stereo vision. In Proceedings of the International Joint Conference on Artificial Intelligence, pp. 674–679, 1981.

## Slide 122: Solving the ambiguity…
Least squares problem:

## Slide 123: Matching patches across images
Overconstrained linear system
  The summations are over all pixels in the K x K window
Least squares solution for d given by

## Slide 124: Conditions for solvability
  Optimal (u, v) satisfies Lucas-Kanade equation
Does this remind you of anything?
When is this solvable? I.e., what are good points to track?
  ATA should be invertible
  ATA should not be too small due to noise
    eigenvalues 1 and  2 of ATA should not be too small
  ATA should be well-conditioned
     1/  2 should not be too large ( 1 = larger eigenvalue)
Criteria for Harris corner detector
Notes: http://en.wikipedia.org/wiki/Invertible_matrix

## Slide 125
Eigenvectors and eigenvalues of ATA relate to edge direction and magnitude
  The eigenvector associated with the larger eigenvalue points in the direction of fastest intensity change
  The other eigenvector is orthogonal to it
M = ATA is the second moment matrix !
(Harris corner detector…)
Notes: Suppose M = vv^T . What are the eigenvectors and eigenvalues? Start by considering Mv

## Slide 126: Low-texture region
gradients have small magnitude
small l1, small l2

## Slide 127: Edge
gradients very large or very small
large l1, small l2

## Slide 128: High-texture region
gradients are different, large magnitudes
large l1, large l2

## Slide 129: Dealing with larger movements: Iterative refinement
  Initialize (x’,y’) = (x,y)
  Compute (u,v) by
  Shift window by (u, v): x’=x’+u; y’=y’+v;
  Recalculate It
  Repeat steps 2-4 until small change
    Use interpolation for subpixel values
2nd moment matrix for feature patch in first image
displacement
It = I(x’, y’, t+1) - I(x, y, t)
Original (x,y) position

## Slide 130: Dealing with larger movements: coarse-to-fine registration
image I
image J
Gaussian pyramid of image 1 (t)
Gaussian pyramid of image 2 (t+1)
image 2
image 1
run iterative L-K
run iterative L-K
upsample
.
.
.

## Slide 131: Shi-Tomasi feature tracker
Find good features using eigenvalues of second-moment matrix (e.g., Harris detector or threshold on the smallest eigenvalue)
  Key idea: “good” features to track are the ones whose motion can be estimated reliably
Track from frame to frame with Lucas-Kanade
  This amounts to assuming a translation model for frame-to-frame feature movement
Check consistency of tracks by affine registration to the first observed instance of the feature
  Affine model is more accurate for larger displacements
  Comparing to the first frame helps to minimize drift
J. Shi and C. Tomasi. Good Features to Track. CVPR 1994.

## Slide 132: Tracking example
J. Shi and C. Tomasi. Good Features to Track. CVPR 1994.

## Slide 133: Summary of KLT tracking
Find a good point to track (harris corner)
Use intensity second moment matrix and difference across frames to find displacement
Iterate and use coarse-to-fine search to deal with larger movements
When creating long tracks, check appearance of registered patch against appearance of initial patch to find points that have drifted

## Slide 134: Implementation issues
Window size
  Small window more sensitive to noise and may miss larger motions (without pyramid)
  Large window more likely to cross an occlusion boundary (and it’s slower)
  15x15 to 31x31 seems typical
Weighting the window
  Common to apply weights so that center matters more (e.g., with Gaussian)

## Slide 135
Picture courtesy of Selim Temizer - Learning and Intelligent Systems (LIS) Group, MIT
Optical flow
Vector field function of the spatio-temporal image brightness variations

## Slide 136: Motion and perceptual organization
Sometimes, motion is the only cue

## Slide 137: Motion and perceptual organization
Even “impoverished” motion data can evoke a strong percept
G. Johansson, “Visual Perception of Biological Motion and a Model For Its Analysis", Perception and Psychophysics 14, 201-211, 1973.

## Slide 138: Motion and perceptual organization
Even “impoverished” motion data can evoke a strong percept
G. Johansson, “Visual Perception of Biological Motion and a Model For Its Analysis", Perception and Psychophysics 14, 201-211, 1973.

## Slide 139: Uses of motion
Estimating 3D structure
Segmenting objects based on motion cues
Learning and tracking dynamical models
Recognizing events and activities
Improving video quality (motion stabilization)

## Slide 140: Motion field
The motion field is the projection of the 3D scene motion into the image
What would the motion field of a non-rotating ball moving towards the camera look like?

## Slide 141: Optical flow
Definition: optical flow is the apparent motion of brightness patterns in the image
Ideally, optical flow would be the same as the motion field
Have to be careful: apparent motion can be caused by lighting changes without any actual motion
  Think of a uniform rotating sphere under fixed lighting vs. a stationary sphere under moving illumination

## Slide 142: Lucas-Kanade Optical Flow
Same as Lucas-Kanade feature tracking, but for each pixel
  As we saw, works better for textured pixels
Operations can be done one frame at a time, rather than pixel by pixel
  Efficient

## Slide 143: Multi-resolution Lucas Kanade Algorithm

## Slide 144: Iterative Refinement
Iterative Lukas-Kanade Algorithm
  Estimate displacement at each pixel by solving Lucas-Kanade equations
  Warp I(t) towards I(t+1) using the estimated flow field
    - Basically, just interpolation
  Repeat until convergence
* From Khurram Hassan-Shafique CAP5415 Computer Vision 2003

## Slide 145: Coarse-to-fine optical flow estimation
image I
image J
Gaussian pyramid of image 1 (t)
Gaussian pyramid of image 2 (t+1)
image 2
image 1
run iterative L-K
run iterative L-K
warp & upsample
.
.
.

## Slide 146: Coarse-to-fine optical flow estimation
image I
image H
Gaussian pyramid of image 1
Gaussian pyramid of image 2
image 2
image 1
u=10 pixels
u=5 pixels
u=2.5 pixels
u=1.25 pixels

## Slide 147: Example
* From Khurram Hassan-Shafique CAP5415 Computer Vision 2003

## Slide 148: Multi-resolution registration
* From Khurram Hassan-Shafique CAP5415 Computer Vision 2003

## Slide 149: Optical Flow Results
* From Khurram Hassan-Shafique CAP5415 Computer Vision 2003

## Slide 150: Optical Flow Results
* From Khurram Hassan-Shafique CAP5415 Computer Vision 2003

## Slide 151: Errors in Lucas-Kanade
The motion is large
  Possible Fix: Keypoint matching
A point does not move like its neighbors
  Possible Fix: Region-based matching
Brightness constancy does not hold
  Possible Fix: Gradient constancy
Notes: Iterative refinement:
Estimate velocity at each pixel using one iteration of Lucas and Kanade estimation
Warp one image toward the other using the estimated flow field
Refine estimate by repeating the process

## Slide 152: State-of-the-art optical flow
Start with something similar to Lucas-Kanade
+ gradient constancy
+ energy minimization with smoothing term
+ region matching
+ keypoint matching (long-range)
Large displacement optical flow, Brox et al., CVPR 2009
Region-based
+Pixel-based
+Keypoint-based

## Slide 153: Stereo vs. Optical Flow
Similar dense matching procedures
Why don’t we typically use epipolar constraints for optical flow?
B. Lucas and T. Kanade. An iterative image registration technique with an application to
stereo vision. In Proceedings of the International Joint Conference on Artificial Intelligence, pp. 674–679, 1981.

## Slide 154: Summary
Major contributions from Lucas, Tomasi, Kanade
  Tracking feature points
  Optical flow
Key ideas
  By assuming brightness constancy, truncated Taylor expansion leads to simple and fast patch matching across frames
  Coarse-to-fine registration

## Slide 155: Orthographic Projection
Special case of perspective projection
  Distance from the COP to the image plane is infinite
  Also called “parallel projection”
  What’s the projection matrix?
Image
World
Slide by Steve Seitz

## Slide 156: Scaled Orthographic Projection
Special case of perspective projection
  Object dimensions are small compared to distance to camera
  Also called “weak perspective”
  What’s the projection matrix?
Image
World
Slide by Steve Seitz

## Slide 157: Annex
Corner Point Detection
Mathematics required for
Optical Flow tracking

## Slide 158: Finding Corners
Key property: in the region around a corner, image gradient has two or more dominant directions
Corners are repeatable and distinctive
C.Harris and M.Stephens. "A Combined Corner and Edge Detector.“ Proceedings of the 4th Alvey Vision Conference: pages 147--151.

## Slide 159: Corner Detection: Mathematics
Change in appearance of window w(x,y)
for the shift [u,v]:
I(x, y)
E(u, v)
E(3,2)
w(x, y)

## Slide 160: Corner Detection: Mathematics
I(x, y)
E(u, v)
E(0,0)
w(x, y)
Change in appearance of window w(x,y)
for the shift [u,v]:

## Slide 161: Corner Detection: Mathematics
Intensity
Shifted intensity
Window function
or
Window function w(x,y) =
Gaussian
1 in window, 0 outside
Source: R. Szeliski
Change in appearance of window w(x,y)
for the shift [u,v]:

## Slide 162: Corner Detection: Mathematics
We want to find out how this function behaves for small shifts
Change in appearance of window w(x,y)
for the shift [u,v]:
E(u, v)

## Slide 163: Corner Detection: Mathematics
Local quadratic approximation of E(u,v) in the neighborhood of (0,0) is given by the second-order Taylor expansion:
We want to find out how this function behaves for small shifts
Change in appearance of window w(x,y)
for the shift [u,v]:

## Slide 164: Corner Detection: Mathematics
Second-order Taylor expansion of E(u,v) about (0,0):

## Slide 165: Corner Detection: Mathematics
Second-order Taylor expansion of E(u,v) about (0,0):

## Slide 166: Corner Detection: Mathematics
Second-order Taylor expansion of E(u,v) about (0,0):

## Slide 167: Corner Detection: Mathematics
The quadratic approximation simplifies to
where M is a second moment matrix computed from image derivatives:
M

## Slide 168
Corners as distinctive interest points
2 x 2 matrix of image derivatives (averaged in neighborhood of a point).
Notation:

## Slide 169: Interpreting the second moment matrix
The surface E(u,v) is locally approximated by a quadratic form. Let’s try to understand its shape.

## Slide 170: Interpreting the second moment matrix
First, consider the axis-aligned case (gradients are either horizontal or vertical)
If either λ is close to 0, then this is not a corner, so look for locations where both are large.

## Slide 171: Interpreting the second moment matrix
Consider a horizontal “slice” of E(u, v):
This is the equation of an ellipse.

## Slide 172: Interpreting the second moment matrix
Consider a horizontal “slice” of E(u, v):
This is the equation of an ellipse.
The axis lengths of the ellipse are determined by the eigenvalues and the orientation is determined by R
direction of the slowest change
direction of the fastest change
(max)-1/2
(min)-1/2
Diagonalization of M:

## Slide 173: Visualization of second moment matrices

## Slide 174: Visualization of second moment matrices

## Slide 175: Interpreting the eigenvalues
1
2
“Corner” 1 and 2 are large, 1 ~ 2; E increases in all directions
1 and 2 are small; E is almost constant in all directions
“Edge” 1 >> 2
“Edge” 2 >> 1
“Flat” region
Classification of image points using eigenvalues of M:

## Slide 176: Corner response function
“Corner” R > 0
“Edge” R < 0
“Edge” R < 0
“Flat” region
|R| small
α: constant (0.04 to 0.06)

## Slide 177: Harris corner detector
Compute M matrix for each image window to get their cornerness scores.
Find points whose surrounding window gave large corner response (f> threshold)
Take the points of local maxima, i.e., perform non-maximum suppression
C.Harris and M.Stephens. “A Combined Corner and Edge Detector.” Proceedings of the 4th Alvey Vision Conference: pages 147—151, 1988.
Notes: 176

## Slide 178: Harris Detector [Harris88]
Second moment matrix
1. Image derivatives
2. Square of derivatives
3. Gaussian filter g(sI)
Ix
Iy
Ix2
Iy2
IxIy
g(Ix2)
g(Iy2)
g(IxIy)
4. Cornerness function – both eigenvalues are strong
har
5. Non-maxima suppression
(optionally, blur first)

## Slide 179: Annex
Some Camera & Human Eye Notions

## Slide 180: Adding a lens
A lens focuses light onto the film
  There is a specific distance at which objects are “in focus”
    other points project to a “circle of confusion” in the image
  Changing the shape of the lens changes this distance
“circle of
confusion”

## Slide 181: The Eye
The human eye is a camera!
  Iris - colored annulus with radial muscles
  Pupil - the hole (aperture) whose size is controlled by the iris
  What’s the “film”?
    photoreceptor cells (rods and cones) in the retina
Slide by Steve Seitz

## Slide 182: The Retina