## Slide 1: Architecture-Mapping Design Space Exploration for DNN Accelerators
Timeloop (Nvidia/MIT) and Zigzag (KU Leuven)
Floran de Putter
Electrical Engineering – Electronic Systems group

## Slide 2: Efficient Deep Learning
Efficient Deep Learning Methods
Model compression
Code transformation
Pruning
Quantization
Compact model
Loop tiling
Loop unrolling
Operator fusion
Goal: Maximize
  Compression Ratio
  Accuracy
  Hardware Usability
Goal: Apply code optimizations to maximize
  Hardware Usability

## Slide 3: Accelerator design considerations
Arithmetic
Data Movement
DRAM
Register
File
*
*
*
*
* *
* *
* *
* *
*
*
*
*
Register
File
Register
File
Register File
*
* * *
On-chip Buffer
PE array
AGUs
Notes: Plaatje kan groter
Slides inspired by Timeloop tutorial

## Slide 4: Data movement
Why it’s important
VGG16 conv 3_2 | 
Multiply Add Ops | 1.85 Billion
Weights | 590 K
Inputs | 803 K
Outputs | 803 K
Energy costs | 
8-bit Integer Multiply | 0.2 pJ
Fetch two 8-bit operands from DRAM | 128 pJ
Fetch two 8-bit operands from large SRAM | 2 pJ
Fortunately…
Reuse

## Slide 5: Exploiting data reuse
Convolutional reuse
  Sliding window over input
Input activation reuse
  Multiple filters over same input
Output activation reuse
  Accumulation sum over channels
Batch reuse
  Re-apply filters to new inputs
7-dimensional network layer
N
.
.
.
N
C
C
K
K
C
P
Weights Inputs
Outputs
S
R
H= Q+S-1
W=P+R-1
.
.
.
Q
Map
DRAM
Buf
RF
*
Temporal
Multicast
Forwarding
Flexible architectures may allow millions of mappings of a single workload
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
2D hardware array
Algorithmic reuse
Hardware reuse

## Slide 6: Mapping choices example
480,000 mappings shown
19x spread in energy efficiency
Only 1 is optimal, 9 others within 1%
6,582 mappings have minimum DRAM accesses
but vary 11x in energy efficiency (how is this possible?)
We need to be able to quickly find the optimal mapping of workload and evaluate it on an architecture
Histogram of the energy efficiency of various mappings of VGG conv3_2 on an example architecture

## Slide 7: Architecture-Mapping Design Space Exploration for DNN Accelerators
Key features of Timeloop and ZigZag:
  Expressive: generic, template-based hardware model
  Fast: faster than native execution
  Accurate: validated against design-specific models
Search space
Mapping
Mapping analysis model
Cost estimator
Search space constructor
Search strategy
(e.g. exhaustive)
Workload
(e.g. Conv2D, FC)
Architecture
(e.g. Eyeriss)
Constraints
(e.g. tile size)
Energy
Best mapping
Technology cost model
(e.g. TSMC 45nm or Accelergy)
Area
Performance
Notes: Ander kleurtje exhaustive

## Slide 8: Overiew
Motivation
General overview
Timeloop
  Examples of mapping, architecture, workload representations
  Search space generator
  Mapping analysis model (tile analysis)
  Cost estimator
ZigZag
Differences between the tools
Summary/conclusion

## Slide 9: Architecture-Mapping Design Space Exploration for DNN Accelerators
Search space
Mapping
Mapping analysis model
Cost estimator
Search space constructor
Search strategy
(e.g. exhaustive)
Workload
(e.g. Conv2D, FC)
Architecture
(e.g. Eyeriss)
Constraints
(e.g. tile size)
Energy
Best mapping
Technology cost model
(e.g. TSMC 45nm or Accelergy)
Area
Performance

## Slide 10: Example 0: workload representation (Conv1D)
for r = [0:R):
for p = [0:P):
Output[p] += Weight[r] * Input[p+r];
P
Weights
Inputs
Outputs
R
W=P+R-1
To represent this…
We write:
problem:
shape:
name: Conv1D
dimensions: [ R, P ]
data-spaces:
- name: Weights
projection:
- [ [R] ]
- name: Inputs
projection:
- [ [P], [R] ]
- name: Outputs
projection:
- [ [P] ]
read-write: True
instance:
R: 3
P: 16

## Slide 11: Example 0: architecture representation
To represent this…
We write:
Buffer
X
PE
architecture: subtree:
- name: PE
local:
- name: Buffer
class: SRAM
attributes:
entries: 64
instances: 1
word-bits: 8
- name: MACC
class: intmac
attributes:
word-bits: 8

## Slide 12: Example 0: mapping representation (Conv1D)
To represent this…
We write:
Buffer
X
PE
mapping:
- target: Buffer
type: temporal
factors: R=3 P=16
permutation: RP
for p = [0:16):
for r = [0:3):
Output[p] += Weight[r] * Input[p+r];
Notes: Add comment: permutation=loop order

## Slide 13: Example 1: 3-level architecture with multiple PEs
architecture:
subtree:
name: System
local:
  name: MainMemory class: DRAM attributes:
......
subtree:
  name: Chip local:
    name: GlobalBuffer class: SRAM attributes:
......
subtree:
- name: PE[0..15]
local:
      name: RegisterFile class: regfile attributes:
......
      name: MACC class: intmac attributes:
......
Main Memory
RegisterFile
X
PE
System
GlobalBuffer
Chip
RegisterFile
X
PE
RegisterFile
X
PE
…
Notes: Font groter / figuur kleiner

## Slide 14: Example 1: mapping (Conv1D + output channels)
mapping:
- target: MainMemory type: temporal factors: R=1 P=1 K=1 permutation: PRK
- target: GlobalBuffer type: temporal factors: R=3 P=1 K=2 permutation: PRK
- target: GlobalBuffer type: spatial factors: R=1 P=1 K=16 permutation: PRK
- target: RegisterFile type: temporal factors: R=1 P=16 K=1 permutation: PRK
for k3 in [0:1) for r3 in [0:1) for p3 in [0:1)
for k2 in [0:2) for r2 in [0:3)
for p2 in [0:1)
spatial_for k1 in [0:16) spatial_for r1 in [0:1) spatial_for p1 in [0:1)
for k0 in [0:1) for r0 in [0:1) for p0 in [0:16)
RegisterFile
MainMemory
GlobalBuffer
Spatial: GlobalBuffer →
RegisterFile
To represent this…
We write:
Notes: k_i is a subtile of k_i+1

## Slide 15: Architecture-Mapping Design Space Exploration for DNN Accelerators
Search space
Mapping
Mapping analysis model
Cost estimator
Search space constructor
Search strategy
(e.g. exhaustive)
Workload
(e.g. Conv2D, FC)
Architecture
(e.g. Eyeriss)
Constraints
(e.g. tile size)
Energy
Best mapping
Technology cost model
(e.g. TSMC 45nm or Accelergy)
Area
Performance

## Slide 16: Search space construction
Unconstrained
Search space
Loop Tiling
Loop Permutation
Loop Permutation
Constrain
Prune
Constrained Search space
Loop Tiling
Loop Permutation
Illegal (tiles won’t fit)
Superfluous (permutations of unit-factors)
Loop Tiling
Pruned, constrained search space
Timeloop travels through the search space using exhaustive or random search heuristics
Notes: Level bypass: bypass a certain memory level

## Slide 17: Architecture-Mapping Design Space Exploration for DNN Accelerators
Search space
Mapping
Mapping analysis model
Cost estimator
Search space constructor
Search strategy
(e.g. exhaustive)
Workload
(e.g. Conv2D, FC)
Architecture
(e.g. Eyeriss)
Constraints
(e.g. tile size)
Energy
Best mapping
Technology cost model
(e.g. TSMC 45nm or Accelergy)
Area
Performance

## Slide 18: Mapping analysis model (tile analysis)
Mapping
tile i
tile i+1
delta
Deltas: set-difference between point sets
Temporal: Indicates stationarity, sliding- window behavior, etc.
Spatial: Indicates overlaps/halos between adjacent units, multicasting/forwarding opportunities
Determines tiles, spatial partitioning of tiles, and schedule
Point sets: at each loop iteration (time step OR instance of a hardware unit)
Tile Analysis: Measure and record deltas over all space and time.
Naïve but robust approach: simulate execution of entire loop nest.
Regular problems:
Compute 1st, 2nd, and last
iterations of each loop
Point sets are Axis-Aligned Hyper Rectangles (AAHR)
for …
for p=[0:8)
for …
for …
Notes: 2 PE’s toevoegen

## Slide 19: Cost estimator
X
PE
System
Chip
X
PE
X
PE
…
For each dataspace:
Tile Accesses
Multicast/Distribution Patterns
Recipient stats
L2
L1
Arithmetic
From Tile Analysis
L3
Multiplier accesses
Buffer accesses
Network transfers
Temporal and spatial accumulations
Address-generator invocations
Derive
Energy: summation of costs for various activities
Performance: Throughput of rate-limiting step
RegisterFile
RegisterFile
RegisterFile
GlobalBuffer
Main Memory

## Slide 20: Architecture-Mapping Design Space Exploration for DNN Accelerators
Search space
Mapping
Mapping analysis model
Cost estimator
Search space constructor
Search strategy
(e.g. exhaustive)
Workload
(e.g. Conv2D, FC)
Architecture
(e.g. Eyeriss)
Constraints
(e.g. tile size)
Energy
Best mapping
Technology cost model
(e.g. TSMC 45nm or Accelergy)
Area
Performance

## Slide 21: Overiew
Motivation
General overview
Timeloop
ZigZag
  Mapping representation
  Loop information extraction
  Cost estimator
  Search space generator
  Memory hierarchy generator
Differences between the tools
Summary/conclusion

## Slide 22: Architecture-Mapping Design Space Exploration for DNN Accelerators
Search space
Mapping
Mapping analysis model
Cost estimator
Search space constructor
Search strategy
(e.g. exhaustive)
Workload
(e.g. Conv2D, FC)
Architecture
(e.g. Eyeriss)
Constraints
(e.g. tile size)
Energy
Best mapping
Technology cost model
(e.g. TSMC 45nm or Accelergy)
Area
Performance

## Slide 23: Example workload representation
ZigZag’s workload is fixed
Loop bounds are configured
Thus, it supports:
  Conv2D
  Conv1D
  Depthwise Conv2D
  Pointwise Conv2D
  Matrix-Vector Multiplication
  Matrix-Matrix Multiplication

## Slide 24: Example architecture representation
Balanced memory hierachy
(at all levels W/I/O are shared)
Unbalanced memory hierachy
(memory level and W/I/O are decoupled)
Both Timeloop and ZigZag support unbalanced memory hierarchies
Notes: Unbalanced corresponds to level bypass in Timeloop

## Slide 25: Example mapping
loop index
Even mapping:
Memory level and loop tiling are coupled
spatially unrolled for-loop
Notes: K=256
C=48
FY/FX=5
OX/OY=26

## Slide 26: Example mapping representation
Even mapping:
Memory level and loop tiling are coupled
Uneven mapping:
Memory level and loop tiling are decoupled
loop index
Note: by supporting uneven mappings, the search space increases dramatically!

## Slide 27: Even vs uneven mappings
Even/uneven temporal mapping’s impact on energy and PE array utilization (throughput) for spatial unrolling: OYu|FYu|Ku=13|5|2

## Slide 28: Architecture-Mapping Design Space Exploration for DNN Accelerators
Search space
Mapping
Mapping analysis model
Cost estimator
Search space constructor
Search strategy
(e.g. exhaustive)
Workload
(e.g. Conv2D, FC)
Architecture
(e.g. Eyeriss)
Constraints
(e.g. tile size)
Energy
Best mapping
Technology cost model
(e.g. TSMC 45nm or Accelergy)
Area
Performance

## Slide 29: Mapping analysis - step 1: loop relevancy
Is the loop bound dependent on the operand W/I/O?
Data reuse possibilities for ir and pr!

## Slide 30: Mapping analysis - step 2
Architecture
Example mapping
130 PE’s

## Slide 31: Mapping analysis - step 3
Many more equations for the other statistics!

## Slide 32: Architecture-Mapping Design Space Exploration for DNN Accelerators
Search space
Mapping
Mapping analysis model
Cost estimator
Search space constructor
Search strategy
(e.g. exhaustive)
Workload
(e.g. Conv2D, FC)
Architecture
(e.g. Eyeriss)
Constraints
(e.g. tile size)
Energy
Best mapping
Technology cost model
(e.g. TSMC 45nm or Accelergy)
Area
Performance

## Slide 33: Search space construction and strategy
Notes: Blocking=tiling

## Slide 34: Search space construction and strategy
Strategies:
  Exhaustively search through all valid mappings
  Heuristic v1 prunes certain loop orders
  Heuristic v2 prunes also certain tile sizes
  Iterative search prunes at each loop assignment iteration beside applying the previous heuristics

## Slide 35: Architecture-Mapping Design Space Exploration for DNN Accelerators
Search space
Mapping
Mapping analysis model
Cost estimator
Search space constructor
Search strategy
(e.g. exhaustive)
Workload
(e.g. Conv2D, FC)
Architecture
(e.g. Eyeriss)
Constraints
(e.g. tile size)
Energy
Best mapping
Technology cost model
(e.g. TSMC 45nm or Accelergy)
Area
Performance
Architecture space

## Slide 36: Memory hierarchy generation

## Slide 37: Timeloop (TL) vs ZigZag (ZZ)
Timeloop
Even mapping
Constrained search space with basic heuristics
Mapping analysis done using ‘fast’ simulation
Cost estimation is fine-grained
ZigZag
Uneven mapping
Search space with advanced heuristics
Mapping analysis done analytically
Cost estimation is course-grained
Memory hierachy generation

## Slide 38: Timeloop (TL) vs ZigZag (ZZ)

## Slide 39: Summary
Key features of Design Space Exploration tools:
  Expressive: generic, template-based hardware model
  Fast: faster than native execution
  Accurate: validated against design-specific models
Both Timeloop and ZigZag allow many architecture-mapping combinations to be evaluated quickly and accurately
ZigZag allows more mappings and has an architecture search space
What about combining NAS and DSE? Covering the Accelerator-Mapping-Network design space