## Slide 1: Intelligent Architectures 5LIL0 Deep Learning Software Tools & Network Design
Berk Ulker
b.ulker@tue.nl
TUEindhoven
2022

## Slide 2: Overview
Deep Learning environment :
  DL tools
  Tool hierarchy, properties
  Network data exchange formats
Network design

## Slide 3: Available Deep Learning Software Frameworks

## Slide 4: Deep learning tools - implementation
API
DL Tools
Backend

## Slide 5: Deep learning stack

## Slide 6: Deep learning stack
High Level API : Provides abstraction for application use
Low level API : Integrate system level support libraries and provide DL functionality
System level support libraries provide efficient kernel implementations of
  Basic linear algebra subprograms (BLAS)
  DNN primitives
  GPU kernels

## Slide 7: Deep learning frameworks
How frameworks are different?
Capabilities : Training, inference, support for multiprocessing
  Focus on different stages of deployment
  Set of available tools / third party tool integration
  Multi-GPU training

## Slide 8: Deep learning frameworks
How frameworks are different?
  Target Platforms
    CPU
    GPU
    TPU
    FPGA

## Slide 9: Deep learning frameworks
  How frameworks are different?
    Network model and execution graph structure

## Slide 10: Deep learning frameworks
    Dynamic computation graph

## Slide 11: Deep learning frameworks
    Differences from static computation graph
    Computational graph is built up dynamically, immediately after we declare variables
    This graph is thus rebuilt after each iteration of training
    Enables computation with different input sizes, without pre-definition
      Natural language processing is a good example, with varying input sizes
    Additional resources used for rebuilding graph

## Slide 12: Deep learning frameworks
How frameworks are different?
  Support, tools and third-party software integration
    Performance analysis tools
      Profilers
    Visualization tools
      Training
      Network architecture
    Library integration
      cuDNN, QNNPACK

## Slide 13: Deep learning frameworks - Popularity
Scores are calculated by combining usage, search volume, related publications, GitHub activity

## Slide 14: Problem : Interoperability
  Typical scenarios include
    Training in and deployment in different frameworks
    Using data or trained network from another framework

## Slide 15: Interoperability
  Translation tools
    Mostly third party implementations
    Need frequent update
  Neural network data exchange formats
    Define operators, computation graph and data format
    Provides single point of synchronization
    ONNX, NNEF

## Slide 16: Why format exchange needed?
Deep learning models are developed in different environments
Training and deployment is often executed in different environments

## Slide 17: Why format exchange needed?
Format Exchange

## Slide 18: Neural Network Exchange Format (NNEF)
  Released by Khronos Group
    Targets conversion from Training tools to inference engines
    Need frequent update
    Not widely supported among frameworks, recently released

## Slide 19: Open Neural Network Exchange (ONNX)
  Initiated by Facebook & Microsoft
    Open source
    Targets software stack flexibility
    Widely supported by DL frameworks
    Many popular pre-trained networks are available ready to use

## Slide 20: Open Neural Network Exchange (ONNX)
PyTorch example

## Slide 21: Overview
Deep Learning environment :
  DL tools
  Tool hierarchy, properties
  Network data exchange formats
Network design :
  Design space
  Tradeoffs
  Common and practical methods

## Slide 22: Network Design
  Designing deep neural networks is still more art than science
    Large design space
    Many architecture solutions for a single problem
  Recent research focuses on
    Automated design
    Guided optimization

## Slide 23: Network Design
  Network design procedure
    Understand problem
    Evaluate application requirements and resource limitations
    Design the architecture
    Training, validation and reiteration

## Slide 24: Design space
  Network design space has many dimensions
    Network size, depth and width
    Operator composition
    Specialized building blocks
    Optimizations

## Slide 25: Common Trade-offs in NN Design
  We can move in design space with tradeoffs on:
    Accuracy / memory use
    Accuracy / latency
    Accuracy / energy consumption
    Energy consumption / speed

## Slide 26: Speed-Accuracy Tradeoff – Object Detection
  We can control these:
    Model complexity
      Detector architecture (e.g., SSD, YOLO, Faster R-CNN etc.)
      Backbone feature extractor (e.g., ResNet, Inception, Mobilenet, VGG)
    Model parameters
      Input resolution
      Number of proposals (for object detection)
    Quantization (e.g., FP32/FP16)

## Slide 27: Speed-Accuracy Tradeoff
Backbone
Detector head
Number of proposals
Input resolution
[Huang et al. Speed/accuracy trade-offs for modern convolutional object detectors]

## Slide 28: Network Optimization Techniques
  Several techniques exist to optimize network execution efficiency
    Pruning
    Quantization
    Weight scaling
    Tensor decomposition

## Slide 29: Network Pruning
  Network pruning is removal of nodes, connections or kernels
    Can be part of the training – learning both
    weights and connections
    Can be adaptively/selectively applied
    Benefits may be limited for non-structured pruning

## Slide 30: Quantization
  Quantization reduces precision of stored data and operators
    Reduce overall memory use
    Compress network, exploiting redundancy
    Supported for several HW platforms with different precision levels
    FP16, INT16, INT8 are most common
    Training may require full precision

## Slide 31: Quantization

## Slide 32: Quantization

## Slide 33: Kernel Decomposition
    Decomposing a kernel into smaller kernels
    Assumes layers are over-parameterized
    CP Decomposition and Tucker Decomposition for convolutional layers
    Operates on a weights of a linear layer
    Applied per layer

## Slide 34: Mobilenet
Standard Conv Cost:
Mobilenet Conv Cost:
Reduction :

## Slide 35: Mobilenet
Activation needs to be used after each convolution
Standard Convolution vs Depthwise Separable Convolution for ImageNet :

## Slide 36: Optimization Problem
  Optimization methods have also “hyperparameters”
    Pruning threshold or percentage
    Quantization level
  How to find optimal values?

## Slide 37: Optimization Problem – Automatizing design
  Search for network architecture can be automatized.
    Need heuristics to narrow down search space
    Need translation of functional requirements or limits to design parameters
      Accuracy
      Execution time
      Memory size
      Energy consumption

## Slide 38: Case study : MorphNet
  MorphNet optimizes an existing network architecture in one shot
    Based on training accuracy and required ops, re-scales layer widths
    Entire filters\layers can be removed
    Guided optimization

## Slide 39: Case study : NetAdapt

## Slide 40: Case study : NetAdapt
Automatically adapts DNN architecture to fit into budget

## Slide 41: Tools and Design
Tools …
Design a CNN network

## Slide 42: Backup / Ideas
Tensorflow workflow

## Slide 43: Tensorflow workflow
https://towardsdatascience.com/top-5-deep-learning-frameworks-to-watch-in-2021-and-why-tensorflow-98d8d6667351