## Slide 1: Extreme quantization beyond int8
Optimizing neural networks for inference
Floran de Putter
Electrical Engineering – Electronic Systems group

## Slide 2: Deep Learning Challenges
Challenge 1: model size
Challenge 2: speed (throughput, latency)
Challenge 3: energy efficiency
We need Efficient Deep Learning!

## Slide 3: Efficient Deep Learning
Efficient Deep Learning Methods
Model compression
Code transformation
Pruning
Quantization
Compact model
Loop tiling
Loop unrolling
Operator fusion
Goal: Maximize
  Compression Ratio
  Accuracy
  Hardware Usability
Goal: Apply code optimizations to maximize
  Hardware Usability

## Slide 4: Basics of Binary/Ternary Neural Networks
Forward pass (XNOR-POPCOUNT during inference)
(Ternary MAC uses similar compute logic: Gated X(N)OR & PopCount)
Backward pass (training only)
  Straight-through estimation (SignSTE)

## Slide 5: Overview
Naive binary neural network
Overview of accuracy repair methods
Specialized accelerators
Summary and conclusion

## Slide 6: Naive BNN: BinaryNet
  VGG9 architecture
  CIFAR10 dataset
  First and last layer remain full precision (orange)
  Convolution and linear (red) are fully binary!
  Binarization using sign-function with clipped STE
  88.6% top-1 accuracy, promising results?
batchnorm
sign
3x3 conv
batchnorm
sign
3x3 conv
batchnorm
sign
3x3 conv
batchnorm
sign
linear
linear
batchnorm
sign
linear
batchnorm
sign
3x3 conv
maxpool
batchnorm
sign
3x3 conv
maxpool
batchnorm
sign
3x3 conv
maxpool

## Slide 7: BinaryNet on ImageNet
Building block:
ResNet-18 architecture
From 69.7% to 42.2% top-1 accuracy on ImageNet…
batchnorm
sign
3x3 conv
batchnorm
sign
3x3 conv
+

## Slide 8: Accuracy of state-of-the-art BNNs
Chart: ResNet-18 based BNNs
| FP ResNet18 | BinaryResNet | ABCNet | GroupNet | ReActNet
Accuracy | 69.7 | 42.2 | 65 | 67 | 65.9
Note: accuracy repair methods do not come for free!

## Slide 9: Overview of accuracy repair methods
Repair methods
Network topology unchanged
Network topology changed
Binarizer (STE)
Normalization
Training strategy
Non-linearity
Scaling factor
Ensemble
Miscellaneous
Extra loss terms

## Slide 10: Ensemble per-layer (Weight only)
  Approximate using linear combination binary filters :
  constructed by shifting () over the standard deviation:
  Scaling parameters found by:
Approximate using 3 binary bases
Conv
BinConv
BinConv
BinConv
+

## Slide 11: Numerical example
Say you want to approximate by three binary bases .
, then bases are:
From, it follows that , thus
Notes: Idea: with binary weights and scaling factors you can recover the original weights.
Python code:
import numpy as np
vec = lambda x: x.flatten() # matrix to vector
sign = lambda x: np.where(x >= 0, 1, -1) # sign activation
# base parameters and input weights
u = [-1, 0, 1]
W = np.array([[-0.135, -0.065],[0.125, 0.075]])
# compute reconstruction
mu, std = np.mean(W), np.std(W, ddof=1)
B = np.array([vec(sign(W - mu + i*std)) for i in u]) # compute bases
a, _, _, _ = np.linalg.lstsq(B.T, vec(W))
W_hat = (B * a[:,None]).sum(axis=0).reshape(W.shape)

## Slide 12: Ensemble per-layer (Activation only)
  Approximate activations like we did with weights:
  constructed using shift vector :
Two examples ():
3 bases;
10 bases;
Notes: import numpy as np
import matplotlib.pyplot as plt
sign = lambda x: np.where(x >= 0, 1, -1) # sign activation
clip = lambda x: np.clip(sign(x), 0, 1)
v1 = np.linspace(-1/5,1/5,3)
v2 = np.linspace(-1,1,10)
x = np.linspace(-10,5,1000)
y1 = np.array([clip(x+i) for i in v1]).sum(axis=0)
y2 = np.array([clip(x+i) for i in v2]).sum(axis=0)
fig,ax = plt.subplots(dpi=80)
ax.scatter(x, y1, marker='.', c='r')
ax.scatter(x, y2, marker='.', c='b')
ax.set_xlabel("x", fontsize=18)
ax.set_ylabel("y", fontsize=18)
ax.set_title("y = sum(clip(x+v_i, 0, 1))", fontsize=18)
plt.xticks(fontsize=14)
plt.yticks(fontsize=14)
ax.spines['right'].set_visible(False)
ax.spines['top'].set_visible(False)
ax.set_xlim([-2,2])

## Slide 13: ABC-Net: ensemble per-layer
  Convolution becomes:
  Workload increases by plus scaling multiplications
  Number of weights increases by times
Approximated convolution
Binary weights and activations
Shifted Sign
BatchNorm
ApproxConv
Shifted Sign
Shifted Sign
ApproxConv
ApproxConv
Weighted Sum
Weighted Sum
BinConv
BinConv
BinConv

## Slide 14: Group-Net: ensemble per-block
  Per-block ensemble
    Quantization error is accumulated less
  Binary base weights are learned
  Workload increases by plus scaling multiplications
  Number of weights increases by times
BinConv
BinConv
BinConv
+
BinConv
BinConv
BinConv
+
ABCNet layer-wise expansion
GroupNet group-wise expansion
BinConv
BinConv
BinConv
BinConv
BinConv
BinConv
+

## Slide 15: ReActNet repairs
Topology changing:
RPReLU
Double Residual
Scaling factor
Topology unchanging:
RSign (normalization)
RSign (STE)
Training strategy
BatchNorm
Binary Conv
+
BatchNorm
Binary Conv
tanh
Binary ResNet
building block
BatchNorm
BinaryConv
+
RSign
BatchNorm
BinaryConv
+
RSign
RPReLU
RPReLU
ReActNet
building block
Sign
Sign

## Slide 16: ReActNet STE

## Slide 17: Specialized BNN/TNN accelerators
Binary:
XNOR Neural Engine
ChewBaccaNN
Mixed-Signal Processor
Ternary:
CUTIE

## Slide 18: XNOR Neural engine – System on Chip overview

## Slide 19: XNE accelerator
Streamer
  TP x 32-bit memory interface for input data, weights, and activations.
  Address generation and word-alignment functionality.
Controller
  Small 28 Byte register file to load layer configuration for execution.
  Small micro-processor to generate loop counters and addresses.
Engine
  XNE datapath that can processor binary convolution and fully-connected layers.
Throughput Parameter TP = 4

## Slide 20: XNE engine
  Dedicated registers for Parameters and Features
    Data reuse
  TP XNORs are computed in parallel
  PopCount can be masked
  16-bit accumulators are used to compute TP pixels in parallel
    Hardwired limitation on TP input/output channels
  Dedicated threshold stage
For TP=128:
  21.6 fJ/Op at 0.4V in 22nm (SCM)
  115 fJ/Op at 0.6V in 22nm (SRAM)
Throughput Parameter TP = 8

## Slide 21: ChewBaccaNN
  Dedicated memory (SCM) for Parameters and Features.
    Row bank for data reuse.
  Compute logic inside BPU array
    A BPU employs shift register for data reuse.
    7 BPUs give a hardwired 7x7 kernel with 16 input channels.
  NMCU accumulates partial results and finally binarizes.

## Slide 22: ChewBaccaNN Floorplan
Total chip area: 0.7 mm2
  Compute units occupy 1%
32 SCM blocks in FMM1
  1 block = 1kB of memory
At 0.4V in 22nm:
  4.48 fJ/Op for 7x7 kernel
  15.38 fJ/Op for 3x3 kernel

## Slide 23: Mixed-Signal Binary CNN Processor
  Mix of digital and analog design
    Accumulation (popcount operation) is analog circuitry
  Hardwired 2x2 kernel with 256 input and output channels
  1.88 fJ/Op at 0.6V&0.8V in 28nm

## Slide 24: CUTIE: Ternary DNN Inference
  Completely unrolled data path w.r.t. all feature map and filter dimensions to reduce data transfer cost
    Immense data reuse!
    Large chip area
  Ternary compression
    5 ternary symbols in 8 bits = 1.6 bits/symbol
  Their TNN has high level of sparsity
    Reduces switching activity
  1.69 fJ/Op at 0.65V in 22nm!

## Slide 25: BNN/TNN accelerator limitations
Most accelerators assume that all data can be stored on-chip
  Not valid for large networks -> costly memory traffic is ignored
Most accelerators assume they can directly calculate an output pixel
  Not valid for large networks -> partial high-bitwidth sums + limited data reuse
Most accelerators cannot skip the thresholding phase
  Needed for state-of-the-art BNNs
Most accelerators fix the amount of input/output channels
  Flexibility issue

## Slide 26: BrainTTA master project: Energy vs flexibilty trade-off
Energy efficiency
Flexibility

## Slide 27: Transport-Triggered Architecture
Example instruction
RF.out → ALU.in1t.add
nop
LSU.out → ALU.in2
Notes: FU
Ports
Busses
Moves; Exposed datapath
Suitable candidate
Minimize data movement
Retaining control
Example instruction
Another flexibility aspect lacking…

## Slide 28: BrainTTA: SoC Overview
Notes: Proposed architecture
TTA core – Compute powerhouse
DMEM/PMEM/IMEM
Banked, wide accesses; next slide
RISC start/stop, mem init
RISC comms outside
Programmed JTAG
Zoom core

## Slide 29: BrainTTA: TTA Core
vMAC
8-bit MAC
  Scalar-Vector MAC
  Vector-Vector MAC
Binary MAC
Ternary MAC
vADD
Vector-Vector addition
Residual support
vOPS
Requantization
Binarization
Ternarization
MaxPool
Auxiliary ops
Notes:   Scalar & Vector datapath
  Load-Store unit
  Banked DMEM PMEM
  Banked IMEM
  vMAC, vADD, vOPS
  Rest for addr calc
  Architecture done, move on to app mapping

## Slide 30: Comparison table
 | ChewBaccaNN | CUTIE |  | XNE |  | Baseline | Optimized
Node (nm) | 22 | 22 |  | 22 |  | 28 | 
Voltage (V) | 0.4 | 0.65 | 0.65 | 0.4 | 0.6 | 0.9 | 0.56
PT (GOPS) | 240 | 16000 | 16000 | 5 | 67 | 880 | 180
Precisions | 1 | 1, T |  | 1 |  | 1, T, 8 | 
E/Op (fJ) | 4.48 – 15.38 | 1.70 | 2.19 | 21.6 | 115 | 101/188/1105 | 59/90/572
Mem tech | SCM | SCM | SRAM | SCM | SRAM | SRAM | 
Mem cap (kB) | 153 | n/a | n/a | 8 | 520 | 1024 | 
Area (mm2) | 0.7 | 7.5 |  | 2.32 |  | 3.6 | 
C multiple of | 16 | 128 |  | 128 |  | 32/16/4 | 
M multiple of | Any | 128 |  | 128 |  | 32/16/32 | 
R is | 7 | 3 |  | Any |  | Any | 
S is | 7 | 3 |  | Any |  | Any | 
Partial result | Yes | No |  | No |  | Yes | 
Programmability | Limited | None |  | Limited |  | C | 
BrainTTA

## Slide 31: Summary and conclusion
BNNs or TNNs might be the holy grail for running DNNs on the edge
MAC can be replaced by cheap bitwise operations: XNOR and Popcount
There is still some research required to make them competitive in terms of accuracy without a large increase in computational workload
State-of-the-art BNN/TNN accelerators achieve down to ~1fJ/Op