## Slide 1: Processor Architectures and Program Mapping
5KK70 TU/e
Henk Corporaal
Bart Mesman
Lab 3
Data Memory Management
Cavity Detection

## Slide 2: Data enters Cavity Detector
scan device
Buffer
serial scan
Cavity
Detector
= image_in
Buffer
image_out =

## Slide 3: Application example
Application domain:
  Computer Tomography in medical imaging
Algorithm:
  Cavity detection in CT-scans
  Detect dark regions in successive images
  Indicate cavity in brain
Bad news for owner of brain

## Slide 4: Application
Reference (conceptual) C code for the algorithm
  all functions: image_in[N x M] -> image_out[N x M]
  new value of pixel depends on its neighbors
  neighbor pixels read from background memory
  approximately 110 lines of C code (ignoring file I/O etc)
  experiments with N x M = 640 x 400 pixels
  straightforward implementation: 6 image buffers
Compute
Edges
Gauss
Blur x
Reverse
Detect
Roots
Max
Value
Gauss
Blur y

## Slide 5: Cavity: main
int main(int argc, char* argv[])
{
static int in_image[N][M];
static int g_image[N][M];
static int c_image[N][M];
static int out_image[N][M];
clock_t starttime, endtime;
read_image(IN_NAME,in_image);
starttime=clock();
GaussBlur(in_image, g_image); // processing starts here
ComputeEdges(g_image, c_image);
DetectRoots(c_image, out_image); // uses reverse and maxval
endtime=clock();
write_image(OUT_NAME,out_image);
printf(" Elapsed time is %f s\n",
1.0*(endtime-starttime) / CLOCKS_PER_SEC);
}

## Slide 6: DMM (data mem. mgt.) principles
Processor
Data Paths
L1
mem/
cache
L2
mem/
cache
Cache
Bank
Combine
local latch 1
& bank 1
local latch N
& bank N
Exploit memory hierarchy
Off-chip SDRAM
Exploit limited life-time of
array elements
Avoid N-port Memories within real-time constraints
Reduce redundant transfers
Introduce Locality
Notes: DTSE is based on analysis of data transfers from/to main memories
Reduce/eliminate redundant transfers: (1) don’t fetch data that you do not need and do not produce data that you will not further use (2) eliminate parts of arrays that are never read/written (dead array access elimination).
Introduce data locality (such that data consumption and production are close together in time and data can be stored locally in FG memory)
Data reuse: exploit memory hierarchy (store data that are frequently accessed in smaller memories closer to the data-paths: less power in smaller memories and less power in transfer)
Avoid N-port memories: bad for power and area. You can usually design a memory architecture with (many) 1-port memories that still meets the cycle-budget constraints for the memory accesses. It happens only very rarely that a solution with an N-port memory is superior to one that contains a number of smaller 1-port memories.

## Slide 7: DMM steps
C-in
Preprocessing
Dataflow transformations
Loop transformations
Data reuse
Memory hierarchy layer assignment
Cycle budget distribution
Memory allocation and assignment
Data layout
C-out
Address optimization

## Slide 8: The DMM steps
Preprocessing
  Rewrite code in 3 layers (parts)
  Selective inlining, Single Assignment form, ....
Data flow transformations
  Eliminate redundant transfers and storage
Loop and control flow transformations
  Improve regularity of accesses and data locality
Data re-use and memory hierarchy layer assignment
  Determine when to move which data between memories to meet the cycle budget of the application with low cost
  Determine in which layer to put the arrays (and copies)
Notes: NOTE on regularity of accesses
Assume you have two loops that produce and consume each other’s data and that they do this in a star pattern as shown below:
This always means that a buffer is needed. It is much better to reverse one of the loops to get a regular access pattern as shown below, in which we may suffice with a small buffer or maybe even a point solution

## Slide 9: The DMM steps
Per memory layer:
Cycle budget distribution
  determine memory access constraints for given cycle budget
Memory allocation and assignment
  which memories to use, and where to put the arrays
Data layout
  determine how to combine and put arrays into memories
Address optimization on the final C-code

## Slide 10: Global loop transformation steps applied to cavity detection
Make all loop dimensions equal
Regularize loop traversal: possibly Y and X loop interchange
  follow order of input stream
Y loop folding and global merging X loop folding and global merging
  full, global scope regularity
  nearly complete locality for main signals (arrays)

## Slide 11: Further hints
You can not merge all loops
  the maxval calculation is blocking you
  with advanced data flow transformations you can get rid of this maxval problem