## Slide 1: Design Technology for Multi-Media Systems (5P600/TD5102) Lab.exercise PMM
Henk Corporaal
Technical University Eindhoven
DTI / NUS Singapore
2003

## Slide 2: Application: YUV-RGB color conversion (part of a Digital Video Decoder)
Slides from Lode Nachtergaele
IMEC Leuven

## Slide 3: Functionality dig.video coder
Y
Cr
Cb
Video
Decoder
101010
010111
100011
RGB
Color
Conversion

## Slide 4: Functionality of color conversion
The routine upsamples color information (Cr and Cb), that is decoded by a video decoder to the size of the luminance information (Y). Then the luminance and chrominance information are transformed to a red, green and blue value for display.

## Slide 5: Driver: YCrCb4:2:0 to RGB
Y
Cr
Cb
2
2
Cr
Cb
2
2
Cr
Cb
Y
RGB

YCrCb
4:2:0
YCrCb
4:2:2
YCrCb
4:4:4

## Slide 6: Size of Y, Cr420 and Cb420 images
// CIF:18*16=288 rows and 22*16=352 cols
#define MBROWS 18
#define MBCOLS 22
unsigned char Y [MBROWS*16][MBCOLS*16];
unsigned char Cr420[MBROWS*8 ][MBCOLS*8 ];
unsigned char Cb420[MBROWS*8 ][MBCOLS*8 ];
Cr
Cb
8
8
16
16
Y
18
22
22
22
18
18

## Slide 7: Size of Cr422 and Cb422 images
// CIF:18*16=288 rows and 22*16=352 cols
#define MBROWS 18
#define MBCOLS 22
unsigned char Y [MBROWS*16][MBCOLS*16];
unsigned char Cr422[MBROWS*16][MBCOLS*8 ];
unsigned char Cb422[MBROWS*16][MBCOLS*8 ];
8
16
Cb
22
18
Cr
22
18

## Slide 8: Size of Cr444 and Cb444 images
// CIF:18*16=288 rows and 22*16=352 cols
#define MBROWS 18
#define MBCOLS 22
unsigned char Y [MBROWS*16][MBCOLS*16];
unsigned char Cr444[MBROWS*16][MBCOLS*16];
unsigned char Cb444[MBROWS*16][MBCOLS*16];
16
16
Cr
18
22
Cb
18
22

## Slide 9: Read Input Data
if ((fp = fopen("akicif.y", "rb")) != NULL) {
fread(Y, sizeof(unsigned char),
(MBROWS*16)*(MBCOLS*16), fp);
fclose(fp);
}
if ((fp = fopen("akicif.u", "rb")) != NULL) {
fread(Cr420, sizeof(unsigned char),
(MBROWS*8)*(MBCOLS*8), fp);
fclose(fp);
}
if ((fp = fopen("akicif.v", "rb")) != NULL) {
fread(Cr420, sizeof(unsigned char),
(MBROWS*8)*(MBCOLS*8), fp);
fclose(fp);
}

## Slide 10: Vertical Upsampling
for (row=0; row < MBROWS*8; row++) {
for (col=0; col < MBCOLS*8; col++) {
Cr422[2*row ][col] =
convolV0(Cr420, col, row-3, row+2);
Cr422[2*row+1][col] =
convolV1(Cr420, col, row-2, row+3);
}
}
Cr
Cb
2
2
Cr
Cb

## Slide 11: Vertical filtering for even columns
unsigned char convolV0(
unsigned char value[MBROWS*8][MBCOLS*8],
int col, int start_row, int stop_row)
{
int i=0, sum=128;
const int coeffs[] =
{3, -16, 67, 227, -32, 7};
for (; start_row+i <= stop_row;i++) {
sum += value[wrap(startRow+i,MBROWS*8)][col]
* coeffs[i];
}
return clip(sum>>8);
}

## Slide 12: Wrap and Clip functions
int
wrap (int coord, int max) {
if (coord < 0) return 0;
if (coord >= max) return max-1;
return coord;
}
unsigned char
clip(int value) {
if (value < 0)
return (unsigned char) 0;
if (value > 255)
return (unsigned char) 255;
return (unsigned char) value;
}

## Slide 13: Horizontal Upsampling
for (row=0; row < MBROWS*16; row++) {
for (col=0; col < MBCOLS*8; col++) {
Cr444[row][2*col ] =
convolH0(Cr422, row,col-3,col+2);
Cr444[row][2*col+1] =
convolH1(Cr422, row,col-2,col+3);
}
}
Cr
Cb
2
2
Cr
Cb

## Slide 14: Horizontal filtering for even rows
unsigned char convolH0(
unsigned char value[MBROWS*16][MBCOLS*8],
int row, int start_col, int stop_col)
{
int i=0, sum=128;
const int coeffs[] =
{5, -21, 70, 228, -37, 11};
for (; start_col+i <= stop_col;i++) {
sum += value[row]
[wrap(start_col+i,MBROWS*8)]*
coeffs[i];
}
return clip(sum>>8);
}

## Slide 15: Color Conversion
Cr
Cb
Y
RGB

unsigned char RGB[MBROWS*16][MBCOLS*16][3];

## Slide 16: Color conversion code
for (row=0; row < MBROWS*16; row++) {
for (col=0; col < MBCOLS*16; col++) {
RGB[row][col][0] =
ycrcb2r( Y[row][col],
Cr444[row][col],
Cb444[row][col]);
RGB[row][col][1] =
ycrcb2g( Y[row][col],
Cr444[row][col],
Cb444[row][col]);
RGB[row][col][2] =
ycrcb2b( Y[row][col],
Cr444[row][col],
Cb444[row][col]);
}
}

## Slide 17: Color convertion functions
unsigned char
ycrcb2r (int y, int cr, int cb) {
const int crv = 104597;
y = 76309 * (y - 16);
return clip((y + crv*(cb-128) +
32768)>>16);
}
unsigned char
ycrcb2g (int y, int cr, int cb) {
const int cgu = 25675;
const int cgv = 53279;
y = 76309 * (y - 16);
return clip((
y-cgu*(cr-128)-cgv*(cb-128)+32768)>>16);
}

## Slide 18: Write RGB image in PPM form
FILE* fp;
if ((fp = fopen("o.ppm", "wb")) != NULL) {
fprintf(fp, "%c%c\n%d %d\n%d\n",
'P', '6',
MBCOLS*16, MBROWS*16,
255);
fwrite(RGB, sizeof(unsigned char),
(MBROWS*16)*(MBCOLS*16)*3,
fp);
fclose(fp);
}